## Slide 1
COMPLETE LEARNING PRESENTATION
AutoCAD Tutorial
Beginner to Advanced
A practical roadmap for 2D drafting, dimensions, layouts, blocks and 3D fundamentals.
MECHANICAL ENGINEERING • PRACTICE-BASED
01

## Slide 2
START HERE
How to use this tutorial
• Follow the modules in order; do not skip drawing setup.
• Type commands at the command line and watch the prompts.
• Complete each practice task before moving to the next module.
• Use millimetres for the mechanical examples in this deck.
• AutoCAD menus and some commands can vary slightly by version.
PRACTICAL TIP
Suggested routine: 20 minutes learning + 30 minutes drawing + 10 minutes checking. Save every practice file with a clear name.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
02

## Slide 3
ROADMAP
Learning roadmap: beginner → advanced
• Level 1 — Interface, coordinates, units and file management.
• Level 2 — Draw and modify 2D geometry accurately.
• Level 3 — Layers, linetypes, text, dimensions and reusable blocks.
• Level 4 — Mechanical drawing workflow, layouts, viewports and plotting.
• Level 5 — Productivity tools, external references and standards.
• Level 6 — Introductory 3D modelling and final portfolio projects.
PRACTICAL TIP
Milestone: create a clean, dimensioned mechanical part drawing on a plotted sheet, then model a simple 3D part.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
03

## Slide 4
MODULE 1
1. What is AutoCAD?
• Computer-aided design (CAD) software used to create precise technical drawings.
• 2D drafting: plans, elevations, sections, details and manufacturing drawings.
• 3D tools: solids, surfaces and visualisation (availability depends on product/version).
• Common users: mechanical, civil, architectural, electrical and manufacturing teams.
• AutoCAD is a drafting tool; engineering decisions still require correct design knowledge.
PRACTICAL TIP
For mechanical engineering, start with accurate 2D drawings before spending much time on 3D.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
04

## Slide 5
MODULE 1
2. Interface essentials
• Drawing area — where geometry is created.
• Command line — type commands and respond to prompts.
• Ribbon/toolbars — grouped tools such as Draw, Modify, Annotate and Layers.
• Status bar — toggles such as Ortho, Object Snap and Dynamic Input.
• Model tab — full-size model; Layout tabs — sheets prepared for printing.
PRACTICAL TIP
If the command line disappears, use Ctrl+9. Learn to read every command prompt instead of clicking randomly.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
05

## Slide 6
MODULE 1
3. Start a drawing correctly
• Use NEW to create a drawing from a suitable template.
• Use UNITS to set length type, precision and insertion scale.
• For this course: decimal units and millimetres for mechanical parts.
• Set LIMITS only if your workflow requires it; zoom extents to view geometry.
• Save early with SAVEAS and use a meaningful filename.
PRACTICAL TIP
Example filename: Bracket_01.dwg. Keep source files and issued PDFs in clearly named folders.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
06

## Slide 7
MODULE 1
4. Coordinate systems
• Absolute coordinates: enter X,Y from the origin; example: 50,30.
• Relative coordinates: prefix with @; example: @40,0.
• Polar coordinates: @distance<angle; example: @60<30.
• Cartesian coordinates are useful for orthogonal shapes and exact locations.
• Use UCS only when you understand how the working coordinate system changes.
PRACTICAL TIP
Try LINE: click or type 0,0 → type @80,0 → @0,40 → @-80,0 → C to close.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
07

## Slide 8
MODULE 1
5. Navigation and precision aids
• ZOOM — change magnification; PAN — move the view.
• OSNAP — snap to endpoints, midpoints, centres, intersections and more.
• ORTHO (F8) — constrain cursor movement horizontally or vertically.
• POLAR (F10) — guide movement at set angles.
• Object Snap Tracking (F11) and Dynamic Input (F12) can speed up accurate work.
PRACTICAL TIP
Use Endpoint, Midpoint, Center and Intersection object snaps deliberately. Avoid estimating locations by eye.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
08

## Slide 9
MODULE 2
6. Core draw commands
• L / LINE — straight segments.
• PL / PLINE — connected segments treated as one polyline.
• C / CIRCLE — circles by centre and radius/diameter options.
• A / ARC — arcs; RECTANG — rectangles; POLYGON — regular polygons.
• H / HATCH — section patterns and filled regions.
PRACTICAL TIP
Practice: draw a 100 × 60 rectangle, a Ø20 circle at its centre, and two Ø8 holes 15 mm from the short edges.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
09

## Slide 10
MODULE 2
7. Core modify commands
• M / MOVE — relocate selected objects.
• CO / COPY — duplicate geometry.
• RO / ROTATE — rotate around a base point.
• MI / MIRROR — create a mirrored copy.
• O / OFFSET — create parallel or concentric geometry.
• TR / TRIM, EX / EXTEND, F / FILLET, CHA / CHAMFER.
PRACTICAL TIP
Mechanical drafting often uses OFFSET, TRIM, FILLET and MIRROR repeatedly. Select objects carefully and confirm the active prompt.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
10

## Slide 11
MODULE 2
8. Selection and editing workflow
• Window selection (left to right): selects objects fully inside the window.
• Crossing selection (right to left): selects objects inside or touched by the boundary.
• Use grips for quick edits, but use exact commands for controlled changes.
• UNDO reverses an action; REDO restores an undone action.
• Use PROPERTIES (Ctrl+1) to inspect and change object properties.
PRACTICAL TIP
If an edit behaves unexpectedly, press Esc to cancel the current command, inspect the selection, and restart.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
11

## Slide 12
MODULE 3
9. Object properties and layers
• Layers organise geometry by function: object, centre, hidden, dimensions and construction.
• Set colour, linetype, lineweight and plot behaviour by layer where possible.
• Use BYLAYER properties to keep drawings consistent.
• Create a sensible layer naming convention and avoid drawing everything on Layer 0.
• Freeze or lock layers when you need to control visibility or prevent edits.
PRACTICAL TIP
Example layers: OBJECT, HIDDEN, CENTER, DIM, TEXT and CONSTRUCTION. Match linetypes and lineweights to your company standard.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
12

## Slide 13
MODULE 3
10. Linetypes, lineweights and visual hierarchy
• Continuous — visible edges and general object geometry.
• Hidden — edges not visible in the current view.
• Center — axes and centres of circles or symmetric features.
• Lineweight differentiates object outlines, dimensions and construction geometry.
• Use LTSCALE and PSLTSCALE thoughtfully when linetypes look incorrect.
PRACTICAL TIP
Check lineweights in Plot Preview. On-screen lineweight display may not match the final printed appearance.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
13

## Slide 14
MODULE 3
11. Text and annotation
• Use TEXT for single-line text and MTEXT for paragraphs or notes.
• Create text styles with consistent font and height settings.
• Use clear notes for material, finish, quantity and manufacturing requirements when specified.
• Keep text readable at the final plotted sheet size.
• Avoid mixing too many fonts or text heights in one drawing.
PRACTICAL TIP
Choose annotation sizes based on the plotted scale and your drawing standard; verify readability in the PDF.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
14

## Slide 15
MODULE 3
12. Dimensioning essentials
• DIMLINEAR — horizontal or vertical dimensions.
• DIMALIGNED — dimensions aligned with a sloped edge.
• DIMDIAMETER and DIMRADIUS — circular features.
• DIMANGULAR — angles; DIMBASELINE and DIMCONTINUE — related dimension series.
• Use DIMSTYLE to control text height, arrows, precision and units.
PRACTICAL TIP
Dimension the design intent: locate features from datums, avoid duplicate dimensions, and do not dimension the same feature twice unnecessarily.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
15

## Slide 16
MODULE 4
13. Engineering drawing conventions
• Use orthographic views to communicate shape: front, top and side.
• Add section views when internal geometry is unclear.
• Show centre lines for holes and symmetric features where appropriate.
• Use hidden lines only when they help communicate the part.
• Follow the drawing standard and company rules for tolerances, symbols and title blocks.
PRACTICAL TIP
AutoCAD does not decide whether a drawing is manufacturable. Check fit, function, tolerances and the intended manufacturing process.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
16

## Slide 17
MODULE 4
14. Blocks and reusable details
• BLOCK combines selected objects into a reusable named object.
• Choose a sensible insertion base point.
• Use INSERT to place a block; SCALE and ROTATE it when appropriate.
• Use WBLOCK to save selected geometry as a separate drawing file.
• Dynamic blocks can expose editable parameters and actions in supported workflows.
PRACTICAL TIP
Create a standard hole/slot symbol or a simple title-block component as your first reusable block.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
17

## Slide 18
MODULE 4
15. Arrays, groups and productivity
• ARRAYRECT — repeat geometry in rows and columns.
• ARRAYPOLAR — repeat around a centre point.
• ARRAYPATH — distribute objects along a path.
• GROUP keeps selected objects together for easier selection.
• Use MATCHPROP to copy properties and PURGE to remove unused definitions when appropriate.
PRACTICAL TIP
Practice: create a bolt-hole pattern using a polar array, then edit the number and spacing of instances.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
18

## Slide 19
MODULE 5
16. Parametric constraints
• Geometric constraints describe relationships such as parallel, perpendicular, tangent and coincident.
• Dimensional constraints control distances, angles, radii and diameters.
• Constraints can help maintain design intent as geometry changes.
• Use them selectively; fully constrained sketches may be more stable but take planning.
• Availability and workflow can vary by AutoCAD version and environment.
PRACTICAL TIP
Try constraining a rectangle so opposite sides remain parallel and adjacent sides remain perpendicular, then set its width and height.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
19

## Slide 20
MODULE 5
17. External references and file coordination
• XREF attaches another drawing as a reference instead of copying its geometry.
• Use references for shared layouts, standard details or coordinated drawings.
• Keep referenced files in predictable folders and use reliable paths.
• Check for missing references before sending or issuing a drawing package.
• Use eTransmit or an equivalent packaging workflow when delivering dependent files.
PRACTICAL TIP
Never assume a DWG is self-contained. Reopen the drawing on another folder or machine to verify that references resolve.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
20

## Slide 21
MODULE 5
18. Layouts, viewports and plotting
• Model geometry at full size in Model space.
• Use Layout/Paper space to arrange the sheet, title block and viewports.
• Set viewport scale and lock the viewport when the view is correct.
• Configure page size, printer/PDF device, plot style and lineweights.
• Always inspect Plot Preview and review the exported PDF before release.
PRACTICAL TIP
Typical workflow: create geometry → set layers/dimensions → open Layout → choose sheet size → set viewport scale → preview → export PDF.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
21

## Slide 22
MODULE 5
19. Drawing quality checks
• Run AUDIT to check and repair drawing database issues when prompted.
• Use PURGE to remove unused named items when safe.
• Check units, scale, dimensions, text, lineweights and missing references.
• Confirm that geometry is closed where required for area, hatch or manufacturing use.
• Compare the plotted PDF with the intended drawing standard.
PRACTICAL TIP
Use a repeatable pre-release checklist. A drawing that looks correct on screen can still plot incorrectly.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
22

## Slide 23
PRACTICE 1
20. Mechanical drafting practice: mounting plate
• Create a 120 × 80 mm rectangular plate.
• Add four Ø10 holes, each 12 mm from the nearest two edges.
• Add a centred Ø25 hole.
• Create OBJECT, CENTER and DIM layers.
• Add dimensions and a note: units in millimetres.
PRACTICAL TIP
Goal: accurate geometry, clean layer use and readable dimensions. Check hole centres numerically before plotting.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
23

## Slide 24
PRACTICE 2
21. Mechanical drafting practice: stepped shaft
• Draw a stepped shaft side view using a clear baseline.
• Use lengths of 25, 40 and 30 mm for three sections.
• Choose diameters such as Ø20, Ø30 and Ø16 for practice only.
• Add centreline, diameter dimensions and overall length.
• Add a simple title block and export a PDF.
PRACTICAL TIP
The values are practice dimensions, not a production design. Real shafts require load, fit, material and tolerance calculations.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
24

## Slide 25
MODULE 6
22. 3D fundamentals: navigation and UCS
• Switch to a 3D workspace or use available 3D tools in your installation.
• Orbit the view to understand the model from different directions.
• Use UCS to define a working coordinate plane when necessary.
• Visual styles such as Wireframe and Shaded change how geometry is displayed.
• Keep the first 3D exercise simple and dimensionally controlled.
PRACTICAL TIP
3D tool availability depends on the AutoCAD product and version. Mechanical 3D design may also be done in dedicated parametric CAD software.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
25

## Slide 26
MODULE 6
23. 3D solid modelling commands
• EXTRUDE — create volume from a closed profile or surface.
• PRESSPULL — push or pull bounded areas where supported.
• REVOLVE — rotate a profile around an axis.
• UNION, SUBTRACT and INTERSECT — combine or compare solids.
• FILLETEDGE and CHAMFEREDGE — modify solid edges.
PRACTICAL TIP
Practice: draw a 40 × 30 rectangle, extrude it 10 mm, then create a cylinder and subtract it to make a simple hole.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
26

## Slide 27
ADVANCED
24. Advanced productivity and automation
• Use command aliases and keyboard shortcuts for frequent operations.
• Use tool palettes for reusable content and standard details.
• Explore scripts or AutoLISP only after you understand the manual workflow.
• Use data extraction where supported to build schedules from drawing objects.
• Document templates, layers and plot settings for consistent team output.
PRACTICAL TIP
Automation should reduce repeat work without hiding errors. Test scripts on a copy of the drawing before using them on production files.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
27

## Slide 28
QUALITY
25. Common beginner mistakes
• Drawing at the wrong unit scale.
• Guessing positions instead of using coordinates and object snaps.
• Leaving all geometry on one layer.
• Using duplicate or conflicting dimensions.
• Forgetting lineweights, page size or plot preview.
• Sending a DWG without its referenced files or a review PDF.
PRACTICAL TIP
When a drawing looks wrong, check units, active layer, object snaps, linetype scale and viewport/plot settings first.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
28

## Slide 29
STUDY PLAN
26. 30-day study plan
• Days 1–5: interface, units, coordinates, navigation and basic draw commands.
• Days 6–10: modify tools, object snaps and precision exercises.
• Days 11–15: layers, linetypes, text and dimension styles.
• Days 16–20: orthographic views, blocks, arrays and drawing conventions.
• Days 21–25: layouts, viewports, plotting, XREF and quality checks.
• Days 26–30: 2D portfolio drawing + introductory 3D model + self-review.
PRACTICAL TIP
Practise daily. Keep one DWG per exercise and export a PDF at the end of each major task so progress is easy to compare.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
29

## Slide 30
CAPSTONE
Final portfolio project
• Choose a simple mechanical component: bracket, plate, pulley or stepped shaft.
• Create clean 2D views with centre lines and appropriate dimensions.
• Organise objects with named layers and reusable blocks where useful.
• Prepare a correctly scaled Layout with title block and plot settings.
• Export a PDF and save the editable DWG with any dependent files.
• Optional: create a simple 3D representation and add screenshots to your portfolio.
PRACTICAL TIP
A strong portfolio shows accuracy, clear communication and a repeatable workflow—not just how many commands you know.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
30

## Slide 31
REFERENCE
Command quick-reference sheet
• Draw: L, PL, C, A, REC, POLYGON, H.
• Modify: M, CO, RO, MI, O, TR, EX, F, CHA.
• Annotate: MTEXT, DIM, DIMSTYLE, LEADER.
• Manage: LA, PROPERTIES, BLOCK, INSERT, XREF.
• View/output: ZOOM, PAN, LAYOUT, PLOT, PUBLISH.
• Check/cleanup: AUDIT, PURGE, DIST, AREA.
PRACTICAL TIP
Command aliases can vary or be customised. If an alias does not work, type the full command name or check your installation settings.
AUTOCAD: BEGINNER TO ADVANCED • MECHANICAL DRAFTING
31

## Slide 32
YOUR NEXT STEP
Open AutoCAD. Draw. Check. Improve.
Start with the mounting plate exercise, complete it without copying the steps, then make a clean plotted PDF.
01
DRAW ACCURATELY
02
ANNOTATE CLEARLY
03
PLOT & CHECK
AutoCAD Tutorial • Beginner to Advanced • Mechanical Drafting Practice
32