## Slide 1
CAD WITH MANUFACTURING
MOULD DESIGN
+ CALCULATIONS
CAD & Mechanical Design • Manufacturing Tools • Materials
MOULD SECTION (SCHEMATIC)
Practical engineering deck | Concepts • Formulas • Examples • Inspection
Educational use: verify production designs against applicable standards and machine/tooling data.

## Slide 2
OVERVIEW
What You Will Learn
02
Learn • Design • Build
01 Mould design fundamentals and core mould elements
02 Calculations: shrinkage, projected area, clamping force and shot volume
03 CAD and mechanical design workflow, drawings, fits and tolerances
04 Manufacturing tools, machining processes and inspection
05 Engineering materials: tool steels, aluminium, plastics and selection factors
Use examples as learning templates—not final production specifications.

## Slide 3
MOULD DESIGN
1. Mould Design: The Big Picture
03
Learn • Design • Build
A mould is a tool that gives material a required shape through a controlled process.
Injection moulding: molten polymer is injected into a closed mould, cooled, and ejected.
Design targets include part quality, repeatability, cycle time, tool life and maintainability.
Inputs: 3D part model, material grade, annual volume, tolerances, surface finish and machine capability.
Start with part and process requirements before choosing the mould architecture.

## Slide 4
MOULD DESIGN
2. Main Elements of an Injection Mould
04
Learn • Design • Build
Cavity
Forms external part surfaces.
Core
Forms internal surfaces, holes and recesses.
Sprue / Runner / Gate
Carries melt from nozzle to cavity.
Cooling channels
Remove heat and help control cycle time.
Ejector system
Releases the part after cooling.
Guide pillars / bushes
Align the mould halves.
Vents
Allow displaced air and gases to escape.
Mould base / plates
Support and locate mould components.

## Slide 5
MOULD DESIGN
3. Parting Line, Draft and Undercuts
05
Learn • Design • Build
Parting line: interface where mould halves meet; choose it to simplify tooling and manage visible witness marks.
Draft angle: taper that helps the part release; the required amount depends on depth, texture and polymer.
Undercut: geometry blocking straight pull; may require slides, lifters or collapsible cores.
Uniform wall thickness helps reduce sink marks, voids, differential cooling and warpage.
Ribs and bosses must be designed carefully to avoid excessive local thickness.
No single draft angle or wall thickness suits every material, texture and geometry.

## Slide 6
MOULD DESIGN
4. Mould Design Workflow
06
Learn • Design • Build
1. Review geometry, material, tolerances, appearance and production quantity.
2. Confirm shrinkage data with the material supplier and define moulding direction.
3. Identify parting line, draft, undercuts, slides/lifters and ejection strategy.
4. Design cavity/core, runner/gate, venting, cooling and support structure.
5. Check machine compatibility: platen, tie-bar spacing, mould height, opening stroke and clamp capacity.
6. Review manufacturability; use flow, cooling or structural analysis when appropriate.
7. Release controlled drawings, BOM, inspection requirements and revision history.

## Slide 7
MOULD CALCULATIONS
5. Calculation: Mould Shrinkage
07
Learn • Design • Build
Formula
Mould dimension ≈ required part dimension ÷ (1 − shrinkage fraction)
Example
Required part length = 100 mm; assumed shrinkage = 1.5% = 0.015
Mould dimension ≈ 100 ÷ (1 − 0.015) = 100 ÷ 0.985 ≈ 101.52 mm
Shrinkage depends on resin grade, process, geometry and flow direction. Use supplier data and mould trials. Confirm the shrinkage convention used by your organization.
Simplified estimate only—not a final mould dimension.

## Slide 8
MOULD CALCULATIONS
6. Calculation: Clamping Force
08
Learn • Design • Build
Formula
Clamp force ≈ projected area × average cavity pressure
Assumptions
Projected area = 120 cm²; average cavity pressure = 40 MPa
120 cm² = 0.012 m²
Force ≈ 0.012 × 40,000,000 = 480,000 N = 480 kN
Actual machine sizing must account for all cavity/runner projected areas, pressure distribution, suitable margin and machine/tooling limits.

## Slide 9
MOULD CALCULATIONS
7. Calculation: Shot Volume
09
Learn • Design • Build
Formula
Total shot volume ≈ (part volume × cavity count) + runner volume
Example
Part volume = 32 cm³; 2 cavities; runner = 8 cm³
Total shot volume ≈ (32 × 2) + 8 = 72 cm³
Check machine shot capacity for the chosen material. Convert volume to mass using material density when needed.
Also consider cushion, screw recovery, runner design and process validation.

## Slide 10
MATERIALS
8. Mould Materials: Starting Guide
10
Learn • Design • Build
P20 / pre-hardened mould steel: common in many general-purpose moulds, depending on grade and service.
H13 / hot-work tool steel: used in demanding tooling where toughness and thermal performance matter.
420 / corrosion-resistant mould steel: considered for corrosive polymers, moisture exposure or high-polish needs.
Aluminium tooling: useful for some prototypes and lower-volume applications; assess wear and temperature limits.
Selection depends on polymer, abrasiveness, corrosion, finish, volume, cooling and repair strategy.
Confirm exact grade, heat treatment and supplier data; trade names and grades vary.

## Slide 11
CAD & MECHANICAL DESIGN
9. CAD & Mechanical Design Workflow
11
Learn • Design • Build
Build a clean parametric model with a stable feature tree and clear design intent.
Use datums, named parameters, appropriate constraints and symmetry where useful.
Check assemblies for interference, clearances, motion and service access.
Create drawings with dimensions, tolerances, datums, surface finish and material/heat-treatment notes.
Use revision control, part numbering, BOMs and manufacturing/inspection feedback.
Validate critical parts with calculations, simulation or physical testing when risk justifies it.

## Slide 12
CAD & MECHANICAL DESIGN
10. Engineering Drawing: Limits and Fits
12
Learn • Design • Build
Basic size
Nominal reference dimension, e.g. 25 mm.
Tolerance
Upper limit − lower limit.
Fit
Clearance, transition or interference relationship.
Hole: 25.000–25.021 mm Shaft: 24.980–24.993 mm
Minimum clearance = 25.000 − 24.993 = 0.007 mm = 7 µm
Maximum clearance = 25.021 − 24.980 = 0.041 mm = 41 µm
Illustrative limits only; select production limits from the applicable standard and functional requirements.

## Slide 13
MANUFACTURING
11. Manufacturing Processes
13
Learn • Design • Build
Turning: cylindrical features such as shafts, pins and bushes.
Milling: faces, pockets, slots and profiles using a rotating cutter.
Drilling, boring and reaming: create or improve holes with different accuracy and finish capabilities.
Grinding: abrasive finishing for suitable tight-size or surface-finish requirements.
EDM / wire EDM: intricate features in electrically conductive materials.
Additive manufacturing: builds parts layer by layer; assess anisotropy, surface finish and post-processing.

## Slide 14
TOOLS & PROCESSES
12. Manufacturing Tools & Cutting Tool Materials
14
Learn • Design • Build
HSS
Tough and versatile; generally lower cutting speeds than carbide.
Cemented carbide
High hot hardness and productivity; setup and vibration matter.
Ceramics / CBN
Used in selected high-speed or hard-material applications.
PCD
Useful for many non-ferrous materials and composites; not for every steel-cutting task.
Coated inserts
Coatings can improve wear and heat performance when matched to the operation.

## Slide 15
MATERIALS
13. Engineering Materials: Quick Map
15
Learn • Design • Build
Carbon / alloy steels
Strength, machinability and heat-treatment options.
Stainless steels
Corrosion resistance varies by grade.
Aluminium alloys
Low density and good machinability; strength varies.
Cast iron
Good damping and machinability in many grades.
Engineering plastics
Low weight; consider creep and thermal expansion.
Copper alloys
Useful thermal/electrical conductivity in selected uses.

## Slide 16
MATERIALS
14. Material Selection Checklist
16
Learn • Design • Build
Function and loads: static, fatigue, impact, wear and stiffness.
Environment: temperature, moisture, chemicals, corrosion and UV exposure.
Manufacturing: casting, machining, forming, welding, heat treatment and finishing.
Economics: material cost, machining time, tool wear, scrap risk and availability.
Quality: strength, hardness, surface finish, dimensional stability and traceability.
Verify the exact grade using an authoritative datasheet and applicable design standard.
Never substitute based on a generic name alone; grade, condition and heat treatment matter.

## Slide 17
INSPECTION
15. Measurement & Quality Tools
17
Learn • Design • Build
Vernier caliper: general outside, inside and depth measurement within its capability.
Outside micrometer: external diameter measurement; check zero and calibration.
Bore gauge: checks internal diameter and can reveal taper or out-of-roundness.
Dial indicator: checks runout, alignment and setup variation.
Surface roughness tester: measures specified surface texture parameters.
CMM / vision system: supports complex geometry inspection with a defined measurement strategy.

## Slide 18
TOOLS & PROCESSES
16. Machining Calculation: Spindle Speed
18
Learn • Design • Build
Formula (metric)
N = (1000 × Vc) ÷ (π × D)
Given
Cutting speed Vc = 120 m/min; tool diameter D = 10 mm
N = (1000 × 120) ÷ (π × 10) ≈ 3,820 rpm
Confirm tool-maker recommendations, workpiece material, tool overhang, coolant, rigidity and machine limits before selecting a setting.
N = spindle speed (rpm) • Vc = cutting speed (m/min) • D = tool diameter (mm)

## Slide 19
DESIGN REVIEW
17. Common Design & Manufacturing Mistakes
19
Learn • Design • Build
Using assumed shrinkage without checking resin grade, flow direction and process conditions.
Choosing a fit code without checking the basic-size range and actual limits.
Leaving insufficient draft, venting, cooling or ejection provisions in a mould.
Applying tight tolerances to non-functional features without a reason.
Selecting tools or materials without considering hardness, heat, wear and rigidity.
Releasing drawings without datums, inspection methods or revision control.
A short design review can prevent expensive tool changes and production delays.

## Slide 20
REVIEW
18. Knowledge Check
20
Learn • Design • Build
1. What are the functions of the cavity and core?
2. Estimate mould dimension for a 60 mm target part size using 1.2% assumed shrinkage.
3. Calculate clamp force for 0.008 m² projected area at 35 MPa average cavity pressure.
4. Which instrument is typically used for precision external diameter measurement?
5. Name two factors that influence material selection.
6. Why are draft and venting important in injection mould design?
Try before checking answers on the next slide.

## Slide 21
REVIEW
19. Knowledge Check — Answers
21
Learn • Design • Build
1. Cavity forms external surfaces; core forms internal features.
2. 60 ÷ (1 − 0.012) = 60 ÷ 0.988 ≈ 60.73 mm (simplified estimate).
3. 0.008 m² × 35,000,000 N/m² = 280,000 N = 280 kN.
4. Outside micrometer, when its range and resolution suit the requirement.
5. Examples: load, temperature, corrosion, wear, density, machinability and cost.
6. Draft helps release; vents allow air/gases to escape and help reduce defects.
Verify calculations and specifications before production use.

## Slide 22
CAD WITH MANUFACTURING
LEARN. DESIGN. BUILD.
Mould design • CAD • Mechanical design
Manufacturing tools • Engineering materials
Follow for practical engineering knowledge
Educational resource • Verify calculations and specifications before production use