## Slide 1
ENGINEERING PROCESS GUIDE
MOULD COMPLETE MANUFACTURING PROCESS
From part design and tool steel to machining, assembly, trials and production
ILLUSTRATED STEP-BY-STEP PPT
Educational reference • Schematics are illustrative, not production drawings
1

## Slide 2
1. Complete Process at a Glance
The typical workflow for an injection mould tool
2
Define the part, resin and production target.
Design the mould and release manufacturing drawings.
Procure certified steel and standard components.
Machine, heat-treat and finish precision details.
Assemble, fit and test the mould.
Run trials, validate parts and release production.
1
Design
2
Steel
3
Machine
4
Fit
5
Trial
6
Validate
Concept → Tooling → Trials → Production readiness
Other mould types—compression, die-casting, blow and transfer—use different tooling details and process controls.

## Slide 3
2. Define the Part & Requirements
Start with the product and production brief
3
Review 3D CAD, 2D drawing, critical dimensions and appearance.
Confirm resin grade, colour, shrinkage data and additives.
Estimate annual volume, target cycle time and tool life.
Identify undercuts, wall thickness, draft and cosmetic zones.
Agree inspection criteria and acceptance limits.
Part geometry & draft
Core / cavity layout
Check shrinkage • parting line • ejection • cooling • venting
Part geometry and resin choice drive the tool design.

## Slide 4
3. Part Design for Mouldability
Resolve design risks before cutting steel
4
Use reasonably uniform wall thickness where possible.
Add draft to vertical faces for reliable release.
Avoid sharp internal corners; use suitable radii.
Place ribs and bosses to limit sink and distortion.
Confirm parting line, gate witness and ejector mark locations.
Part geometry & draft
Core / cavity layout
Check shrinkage • parting line • ejection • cooling • venting
Draft and wall recommendations depend on resin, texture and geometry.

## Slide 5
4. Mould Concept & Layout
Choose a tool architecture that fits the job
5
Choose single-cavity or multi-cavity layout.
Select two-plate, three-plate or hot-runner arrangement.
Plan core, cavity, parting line and shut-offs.
Locate sprue, runner, gate, vents and cooling circuits.
Check press size, tie-bar spacing, opening stroke and ejection stroke.
1
Design
2
Steel
3
Machine
4
Fit
5
Trial
6
Validate
Concept → Tooling → Trials → Production readiness
Confirm the press and mould interface before detailed design.

## Slide 6
5. Mould Design & Engineering Checks
CAD, simulation and detail drawings
6
Design core and cavity using the part model and shrinkage allowance.
Check slides, lifters and other side-action mechanisms.
Size cooling channels for balanced heat removal.
Design ejector pins/plates and safe return mechanisms.
Review mould strength, alignment, venting and service access.
Use filling/warpage simulation when complexity or risk warrants it.
Part geometry & draft
Core / cavity layout
Check shrinkage • parting line • ejection • cooling • venting
Final shrinkage and process values must be based on the actual resin supplier and trials.

## Slide 7
6. BOM & Manufacturing Planning
Release drawings and plan operations
7
Create a bill of materials (BOM) for plates, inserts and standards.
Set material grades, hardness and surface-finish requirements.
Define datum scheme, tolerances and inspection points.
Prepare operation routing, setup sheets and tool lists.
Plan heat treatment, EDM, grinding and coating where needed.
Clamp
Cavity
Core
Ejector
Support
Clamp
Align datums • fit leaders • verify free movement
Keep revision control between CAD, drawings, BOM and CNC programs.

## Slide 8
7. Tool Steel & Component Procurement
Material quality affects tool life
8
Choose suitable mould steel for resin, corrosion and wear conditions.
Common options include P20, 420 stainless, H13 and hardened tool steels.
Select pre-hardened or heat-treatable grade as design requires.
Order standard parts: guide pillars, bushes, ejectors and fittings.
Verify material certificates, dimensions and traceability on receipt.
Certified tool steel
MATERIAL CERT.
Select grade for resin, volume, wear, corrosion and required life
Grade selection is application-specific; consult supplier data and toolmaker requirements.

## Slide 9
8. Cutting Stock & Preparation
Prepare blanks before precision machining
9
Cut steel blanks with machining allowance.
Mark part numbers, material grade and orientation.
Square and face plates to establish datums.
Check stock condition and remove burrs safely.
Record incoming dimensions and material identification.
CNC milling / drilling
EDM / wire EDM
Rough machine → semi-finish → finish machine
Leave suitable allowance for heat treatment and finishing operations.

## Slide 10
9. CNC Milling & Drilling
Create the main mould geometry
10
Rough-machine plates, pockets and insert seats.
Semi-finish and finish core/cavity profiles.
Machine holes for guide pillars, bushes and fasteners.
Drill cooling channels and ports as designed.
Use workholding and toolpaths that control distortion.
CNC milling / drilling
EDM / wire EDM
Rough machine → semi-finish → finish machine
Use approved feeds, speeds, coolant and guarding for the machine and material.

## Slide 11
10. EDM & Wire EDM
Machine details that cutters cannot reach
11
Use sinker EDM for deep ribs, sharp internal details and complex pockets.
Use wire EDM for accurate through-profiles and inserts.
Prepare electrodes and compensate for the required spark gap.
Control recast layer and surface integrity where critical.
Inspect EDM dimensions and finish before polishing.
CNC milling / drilling
EDM / wire EDM
Rough machine → semi-finish → finish machine
EDM parameters and post-processing depend on steel grade and required surface quality.

## Slide 12
11. Heat Treatment & Stress Relief
Stability and hardness must be controlled
12
Apply stress relief or hardening only as specified for the steel.
Use a qualified heat-treatment supplier and documented cycle.
Control distortion; plan allowance for post-treatment grinding.
Verify hardness at specified locations.
Inspect cracks, dimensions and material traceability after treatment.
Certified tool steel
MATERIAL CERT.
Select grade for resin, volume, wear, corrosion and required life
Not every steel or component needs the same heat-treatment route.

## Slide 13
12. Grinding, Lapping & Polishing
Achieve fit and required surface finish
13
Grind datums, shut-offs and mating surfaces to tolerance.
Lap critical sealing and sliding surfaces where required.
Polish cavity surfaces to the specified texture or gloss.
Protect sharp edges and avoid rounding shut-off details.
Measure flatness, parallelism and surface finish.
Milled
Ground
Polished
Measure: dimensions • flatness • surface finish
Cosmetic texture may require chemical etching, laser texturing or other approved finishing.

## Slide 14
13. Cooling System Manufacture
Build and verify the heat-removal system
14
Machine drilled or conformal cooling passages per design.
Deburr and clean channels to prevent blockage.
Install plugs, baffles, bubblers and connectors as specified.
Pressure-test circuits and check for leakage.
Label inlet/outlet circuits and confirm flow direction.
Balanced cooling circuit
Pressure-test channels before assembly
Cooling layouts must account for strength, sealing and serviceability.

## Slide 15
14. Vents, Gates & Runner Details
Control filling and trapped air
15
Machine gate and runner dimensions to the approved design.
Provide vents at likely air-trap and end-of-fill locations.
Avoid excessive vent depth that could cause flash.
Keep vent paths clean and accessible for maintenance.
Review gate location for weld lines, packing and appearance.
Part geometry & draft
Core / cavity layout
Check shrinkage • parting line • ejection • cooling • venting
Vent dimensions and gate sizes depend on resin, geometry and process window.

## Slide 16
15. Ejection & Side Actions
Release the part without damage
16
Machine ejector holes and guide features accurately.
Fit pins, sleeves, blades or stripper systems as designed.
Check slides, lifters, angle pins and wear plates.
Verify clearance, lubrication and full travel.
Ensure ejectors return before the next mould close.
Pins / sleeves / stripper plate must move freely
Avoid ejector placement on fragile or highly visible part surfaces where possible.

## Slide 17
16. Bench Fitting & Assembly
Fit components into a complete mould
17
Clean all components and remove burrs before assembly.
Install inserts, leaders, bushes and locating features.
Check parting-line contact and shut-off blueing where appropriate.
Verify slide/lifter motion and ejector return.
Torque fasteners to the approved specification and protect moving surfaces.
Clamp
Cavity
Core
Ejector
Support
Clamp
Align datums • fit leaders • verify free movement
Use lifting equipment and lockout procedures when handling heavy mould components.

## Slide 18
17. Pre-Trial Inspection
Check the tool before mounting it
18
Confirm dimensions, hardness and critical fits against drawings.
Inspect cooling circuits for flow and leaks.
Check water, hydraulic, pneumatic and electrical connections.
Verify mould opening, closing and ejection by safe dry cycling.
Complete the pre-trial checklist and record open issues.
Dimensional inspection
CHECKLIST
Record actual values against drawing tolerances
Never bypass machine interlocks or guards during checks.

## Slide 19
18. First Mould Trial (T0/T1)
Run a controlled first shot and observe
19
Mount and clamp the mould using approved procedures.
Set resin drying and machine parameters from validated guidance.
Start conservatively and adjust within safe process limits.
Inspect fill, flash, sink, weld lines, warpage and ejection.
Record machine settings, sample IDs and defects.
Trial press
Molded sample
Fill
Flash
Dimensions
Ejection
Only trained personnel should operate the press and handle hot material.

## Slide 20
19. Troubleshooting & Tool Corrections
Fix the cause, not only the symptom
20
Short shot: review venting, fill balance, gate and process settings.
Flash: check parting-line contact, clamp force and process pressure.
Sink/voids: review packing, gate freeze, wall thickness and cooling.
Warpage: review cooling balance, packing and part geometry.
Ejector marks: review pin position, contact area and release.
Trial press
Molded sample
Fill
Flash
Dimensions
Ejection
Change one variable at a time where practical and document each change.

## Slide 21
20. Validation & Production Release
Prove that the tool meets requirements
21
Measure critical-to-quality dimensions across multiple shots.
Confirm appearance, assembly fit and functional performance.
Check repeatability over a representative run.
Approve process window, cycle time and quality plan.
Release tool documentation, maintenance plan and sample approval.
Dimensional inspection
CHECKLIST
Record actual values against drawing tolerances
Sampling quantity and capability criteria should follow the customer quality plan.

## Slide 22
21. Production Operation
Run stable, repeatable cycles
22
Dry and handle resin according to supplier instructions.
Set validated temperatures, pressure, speed and cooling time.
Monitor first-off parts and scheduled quality checks.
Track cycle time, scrap, alarms and cavity-to-cavity variation.
Keep the mould clean and follow safe changeover procedures.
Dry resin
Set machine
Mould
Inspect
Monitor cycle time, scrap, cavity balance and tool wear
Use the approved process sheet; do not rely on generic settings alone.

## Slide 23
22. Preventive Maintenance & Tool Life
Maintain the mould after production
23
Clean vents, parting lines and resin deposits using approved methods.
Inspect gates, ejectors, slides, guide parts and wear surfaces.
Check cooling flow, corrosion, leakage and blocked passages.
Lubricate specified moving parts and replace worn standards.
Log shots, repairs, changes and next service due date.
Clean & inspect
PM CHECKLIST
Clean vents
Check wear
Check cooling
Lubricate
Preventive maintenance protects quality and tool life
Maintenance frequency depends on resin, production conditions and tool design.

## Slide 24
23. Manufacturing Process Checklist
Use this as a practical project review before production release
24
Design
Approved CAD, drawings, resin, shrinkage and press interface
Material
Correct steel grade, certificates, traceability and hardness plan
Machining
CNC/EDM operations complete; critical dimensions inspected
Finishing
Required texture, polish, flatness and shut-off fit verified
Systems
Cooling leak test; vents clear; ejection and side actions free
Trial
Samples, process settings, defects and corrections documented
Release
Part approval, process window, BOM and maintenance plan issued

## Slide 25
KEY TAKEAWAYS
A mould is successful when its design, machining, fit, cooling, ejection and process settings work together.
Design for manufacturability before steel cutting.
Control datums, tolerances, hardness and surface finish.
Trial systematically and use measured evidence for corrections.
Document the validated process and maintain the tool preventively.
Always follow approved drawings, machine manuals, material data and workplace safety procedures.
26