## Slide 1
CAREER & TECHNICAL SKILLS
DIPLOMA MECHANICAL ENGINEER INTERVIEW PREPARATION
Complete study guide: core concepts, formulas, workshop knowledge, HR questions and mock interviews.
TECHNICAL + HR + PRACTICAL
For diploma holders preparing for fresher and junior technician/engineer roles

## Slide 2
1. How to Use This Interview Guide
A practical revision plan
2
Revise basic definitions and formulas first.
Practise explaining concepts in simple words.
Prepare examples from workshop, internship or college projects.
Answer safety and quality questions with practical steps.
Use mock questions and speak answers aloud.
Never claim experience or skills you do not have.
Concept
Formula
Unit
Application
Understand the principle before the formula

## Slide 3
2. Tell Me About Yourself
Build a 45–60 second introduction
3
State your diploma branch and graduation year.
Mention 2–3 relevant subjects: manufacturing, drawing, materials or maintenance.
Describe one real project, internship or workshop task.
Name practical skills you can demonstrate honestly.
Finish with the role you want and willingness to learn.
Clear answer • relevant example • confidence
Template: “I completed a Diploma in Mechanical Engineering. I’m interested in [role]. My strengths are [skills], and in [project/training] I learned [specific task]. I’m looking for an opportunity to apply these basics and grow.”

## Slide 4
3. Common HR Questions
Prepare truthful, concise answers
4
Why did you choose mechanical engineering? Connect interest to machines, design or manufacturing.
What are your strengths? Give one example that proves each strength.
What is your weakness? Choose a real, manageable skill you are improving.
Why should we hire you? Link your basics and learning attitude to the role.
Are you willing to work shifts or relocate? Answer honestly.
What are your salary expectations? Ask about the role’s approved range and total package.
Clear answer • relevant example • confidence

## Slide 5
4. Engineering Fundamentals
Units, dimensions and core terms
5
Force: newton (N); work/energy: joule (J); power: watt (W).
Pressure: pascal (Pa); stress: N/mm² or MPa.
Torque: N·m; speed: rpm; temperature: °C or K.
Mass is measured in kg; weight is a force measured in N.
Accuracy is closeness to reference; precision is repeatability.
Always state units and assumptions when solving a problem.
Concept
Formula
Unit
Application
Understand the principle before the formula

## Slide 6
5. Engineering Mechanics
Force, moment, friction and equilibrium
6
Newton’s laws explain motion and the relation between force and acceleration.
Moment = force × perpendicular distance from pivot.
For static equilibrium: sum of forces = 0 and sum of moments = 0.
Friction opposes relative motion or the tendency to move.
Stress = force / area; strain = change in length / original length.
Draw a free-body diagram before solving force problems.
Mechanical systems • motion • power

## Slide 7
6. Strength of Materials
Stress, strain and elastic behaviour
7
Tensile stress = axial load / cross-sectional area.
Normal strain = change in length / original length.
Within linear elastic range: Young’s modulus = stress / strain.
Yield strength marks onset of significant plastic deformation.
Factor of safety = strength limit / design stress (basis must be specified).
Bending, torsion, fatigue and buckling are different failure modes.
Mechanical systems • motion • power
Use consistent units and the correct loading model.

## Slide 8
7. Thermodynamics Basics
Heat, work and energy
8
Temperature indicates thermal state; heat is energy transfer due to temperature difference.
First law: energy is conserved.
For a closed system: ΔU = Q − W when W is work done by the system.
Specific heat is energy needed to raise unit mass by one degree.
Efficiency = useful output / input × 100%.
Differentiate heat engine, refrigerator and heat pump.
Heat transfer and temperature

## Slide 9
8. Heat Transfer
Conduction, convection and radiation
9
Conduction transfers energy through a material due to a temperature gradient.
Convection transfers energy between a surface and moving fluid.
Radiation transfers energy through electromagnetic waves.
For 1-D conduction, heat rate depends on area and temperature gradient.
Insulation reduces heat transfer; fins increase surface area for convection.
Real systems may combine all three modes.
Heat transfer and temperature

## Slide 10
9. Fluid Mechanics & Hydraulics
Pressure, flow and practical systems
10
Pressure = force / area; hydrostatic pressure increases with depth.
Continuity for incompressible steady flow: A₁V₁ = A₂V₂.
Bernoulli’s equation applies under defined ideal-flow assumptions.
Hydraulic force (ideal) = pressure × piston area.
Pneumatics use compressed gas; hydraulics use liquid under pressure.
Leaks and contamination can reduce system performance.
Pressure × area = ideal force

## Slide 11
10. Manufacturing Processes
How parts are made
11
Casting: molten material solidifies in a mould.
Forging: material is shaped mainly by compressive forces.
Rolling: material passes between rolls to reduce thickness or shape section.
Machining removes material using cutting tools.
Welding joins parts through heat, pressure or both.
Powder metallurgy forms parts from powder through compaction and sintering.
Turning • milling • drilling • grinding

## Slide 12
11. Lathe, Milling & Drilling
Know machine purpose and operations
12
Lathe: workpiece rotates; common operations include turning, facing and threading.
Milling: rotating multi-point cutter removes material.
Drilling creates a hole; reaming improves hole size and finish.
Boring enlarges or corrects an existing hole.
Grinding uses an abrasive wheel for finishing and accuracy.
Identify workholding, cutting tool, feed, speed and coolant requirements.
Turning • milling • drilling • grinding

## Slide 13
12. Cutting Speed & RPM Formula
A frequent workshop calculation
13
N = (1000 × V) / (π × D) for metric cutting speed.
N = spindle speed in rpm; V = cutting speed in m/min; D = diameter in mm.
Example: V = 30 m/min and D = 10 mm.
N ≈ (1000 × 30) / (3.1416 × 10) ≈ 955 rpm.
Choose a suitable available machine speed and follow tool guidance.
Clamp the workpiece; never hold it by hand while drilling.
Measure • compare • record
Illustrative example; actual cutting speed depends on tool, material and operation.

## Slide 14
13. Metrology & Measuring Instruments
Choose the right instrument
14
Steel rule: quick, lower-precision length checks.
Vernier caliper: external, internal and depth measurements within its range.
Micrometer: precise thickness or diameter measurement.
Dial indicator: small displacement, runout and alignment checks.
Height gauge and surface plate: height and layout measurements.
Use clean, calibrated instruments and avoid excessive measuring force.
Measure • compare • record

## Slide 15
14. Limits, Fits & Tolerances
Essential for assembly and interchangeability
15
Tolerance is the permitted variation in a dimension.
Clearance fit: clearance exists between mating parts.
Interference fit: assembly requires force or a suitable thermal method.
Transition fit may result in clearance or interference depending on actual sizes.
Hole-basis system commonly keeps basic hole size fixed and varies shaft limits.
Read drawing symbols and datums; do not guess unspecified tolerances.
Measure • compare • record

## Slide 16
15. Engineering Drawing & GD&T
Read the drawing before making the part
16
Orthographic views communicate geometry; isometric views help visualize shape.
Section views reveal internal features.
Dimensions define size and location; tolerances define allowed variation.
Surface-finish symbols indicate required surface texture.
Datums establish references for measurement and geometric control.
Check revision, units, material, heat treatment and notes.
Resume • projects • skills

## Slide 17
16. Materials & Heat Treatment
Select materials for service conditions
17
Steel is an iron-based alloy with carbon and possibly other alloying elements.
Cast iron generally has higher carbon content and useful casting behaviour.
Aluminium alloys are lightweight; stainless steels can provide corrosion resistance.
Hardness resists indentation; toughness is energy absorbed before fracture.
Annealing, normalizing, hardening and tempering produce different effects.
Material choice depends on load, wear, corrosion, temperature, cost and manufacturability.
Mechanical systems • motion • power

## Slide 18
17. Welding & Fabrication
Basic shop-floor questions
18
Common processes include SMAW (stick), GMAW/MIG, GTAW/TIG and resistance welding.
Defects can include porosity, cracks, lack of fusion or undercut.
Prepare joint edges and clean surfaces as required by the procedure.
Use specified welding procedure, consumables and inspection method.
PPE includes suitable helmet, gloves, protective clothing and ventilation.
Never weld unknown containers without authorized safe preparation.
Welding processes and safe practice

## Slide 19
18. CNC, CAD & CAM Basics
Useful skills for manufacturing roles
19
CAD creates 2D drawings and 3D models.
CAM creates toolpaths from geometry and manufacturing strategy.
CNC machines execute programmed motion using controlled axes.
G-code and M-code functions depend on controller and machine.
Check work offset, tool offset, program revision, fixture and simulation before running.
Only operate machines after appropriate training and authorization.
Turning • milling • drilling • grinding

## Slide 20
19. Quality Control & Inspection
Prevent defects and prove conformity
20
Inspection compares a product with drawings and specifications.
Quality assurance focuses on planned systems; quality control checks outputs.
Calibration links instrument readings to known references.
5S: Sort, Set in order, Shine, Standardize, Sustain.
Root-cause tools include 5 Whys, fishbone diagrams and Pareto analysis.
Record nonconformities, contain affected parts and follow corrective action.
CHECK SHEET
Process control
Quality • safety • delivery • cost

## Slide 21
20. Maintenance & Troubleshooting
Reliability is a practical engineering skill
21
Breakdown maintenance occurs after failure; preventive maintenance is scheduled.
Predictive maintenance uses condition information such as vibration or temperature.
Lubrication reduces friction and wear when the correct lubricant and interval are used.
For a fault: make safe, collect evidence, check likely causes, test and document.
Use lockout/tagout or the site’s energy-isolation procedure before maintenance.
Never remove guards or bypass interlocks to save time.
Stop • isolate • verify • report

## Slide 22
21. Industrial Safety
Safety answers should be practical
22
Identify hazards before starting a task and follow the risk assessment.
Wear task-appropriate PPE and use machine guards.
Isolate energy sources before servicing equipment.
Use approved lifting equipment and never stand under suspended loads.
Report near misses, unsafe conditions and injuries promptly.
If unsure, stop and ask a competent supervisor.
Stop • isolate • verify • report

## Slide 23
22. Role-Specific Preparation
Adapt revision to the job description
23
Production: cycle time, output, rejection, 5S and standard work.
Quality: drawing interpretation, instruments, sampling and nonconformance.
Maintenance: fault finding, lubrication, alignment and energy isolation.
CNC/operator: tooling, offsets, workholding, feeds/speeds and program checks.
Design: CAD, tolerances, material selection and design intent.
Tool room/mould: mould components, fit, cooling, ejection and maintenance.
Concept
Formula
Unit
Application
Understand the principle before the formula

## Slide 24
23. Project & Internship Questions
Turn experience into evidence
24
What was the objective and what problem did you solve?
What was your personal contribution—not only the team’s work?
Which material, process, tools or software did you use?
What constraints, errors or safety risks did you handle?
What result can you show or quantify?
If you would improve it, what would you change and why?
Resume • projects • skills

## Slide 25
24. Mock Technical Interview — Round 1
Practise aloud; answers should be concise
25
What is the difference between stress and strain?
Explain clearance, interference and transition fits.
Why is coolant used in machining?
What is the difference between welding and brazing?
Explain conduction, convection and radiation.
How do you calculate drilling spindle speed?
Name three measuring instruments and their uses.
Clear answer • relevant example • confidence
Practise answering in 30–60 seconds, then add a real workshop example.

## Slide 26
25. Mock Technical Interview — Round 2
Troubleshooting and practical judgement
26
A drilled hole is oversized. What would you check?
A bearing runs hot. What possible causes would you investigate?
A component fails dimensional inspection. What is your first action?
A hydraulic cylinder moves slowly. What checks are appropriate?
A machine vibrates more than usual. How do you respond safely?
A drawing and verbal instruction conflict. What do you do?
CHECK SHEET
Process control
Quality • safety • delivery • cost
Strong answers include safety, evidence, systematic checks and escalation.

## Slide 27
26. Model Answer Framework
Structure answers so the interviewer can follow
27
Define the concept in one sentence.
Explain how it works or why it matters.
Give one practical example from a machine, part or project.
Mention a limitation, safety factor or quality check if relevant.
For troubleshooting: safety → symptoms → likely causes → tests → corrective action.
If you do not know, say so and explain how you would find the answer.
Concept
Formula
Unit
Application
Understand the principle before the formula

## Slide 28
27. Resume & Documents Checklist
Prepare before interview day
28
One-page resume with accurate education, skills and project details.
Diploma marksheets, certificates and identity documents as requested.
Project summary, drawings, photos or portfolio if permitted.
Know your resume: every listed tool and software may be discussed.
Keep copies and digital backups; follow employer instructions.
Plan travel and arrive early; dress neatly and communicate respectfully.
Resume • projects • skills

## Slide 29
28. Final Revision Formula Sheet
Review units and formulas—not just memorized answers
29
Moment = Force × perpendicular distance.
Stress = Force / Area; strain = ΔL / L₀.
Power = Work / Time; efficiency = output / input × 100%.
Pressure = Force / Area; hydraulic force ≈ pressure × piston area.
Continuity for incompressible flow: A₁V₁ = A₂V₂.
Spindle speed: N = (1000 × cutting speed) / (π × diameter).
Concept
Formula
Unit
Application
Understand the principle before the formula

## Slide 30
29. Quick Self-Test
Try answering before checking the answer key
30
1
Which instrument is commonly used for precise small-diameter measurement?
2
What does a clearance fit guarantee?
3
Name the three main modes of heat transfer.
4
What should happen before machine maintenance?
5
What is the unit of torque?
6
What does CNC stand for?

## Slide 31
30. Quick Self-Test — Answer Key
Check your understanding
31
1
Outside micrometer, when suitable for the size and tolerance.
2
A positive gap between mating parts at specified limits.
3
Conduction, convection and radiation.
4
Isolate hazardous energy using the approved procedure and verify safe state.
5
Newton-metre (N·m).
6
Computer Numerical Control.

## Slide 32
YOUR INTERVIEW PREPARATION PLAN
Day 1
Self-introduction, HR questions and resume.
Day 2
Mechanics, strength of materials and formulas.
Day 3
Manufacturing, machines, materials and metrology.
Day 4
Quality, maintenance, CAD/CNC and safety.
Day 5
Mock interview, project story and final revision.
Know the basics • Speak honestly • Think safely • Keep learning
32