## Slide 1
GD&T
GEOMETRIC DIMENSIONING
& TOLERANCING
Complete Mechanical Engineering Guide
Symbols • Datums • Feature Control Frames • Tolerance Zones • Inspection • Worked Examples
⌖
⌀0.10
A
B
For Diploma / BE / B.Tech
Design • Quality • Manufacturing
Illustrations are schematic. Always follow the drawing standard and revision specified by your organization.
GD&T • Geometric Dimensioning & Tolerancing
01

## Slide 2
1. Learning Objectives
What you will be able to do after this presentation
• Understand why geometric tolerances are used beyond size tolerances.
• Read feature control frames (FCFs), datum references and common symbols.
• Distinguish form, orientation, location, profile and runout controls.
• Understand tolerance zones, MMC/LMC/RFS concepts and bonus tolerance.
• Plan inspection using gauges, indicators, CMMs and functional fixtures.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
Read the control, identify the datum, understand the zone.
GD&T • Geometric Dimensioning & Tolerancing
02

## Slide 3
2. What Is GD&T?
Definition and purpose
• GD&T is a symbolic language used on engineering drawings to define allowable geometric variation.
• It controls form, orientation, location, profile and runout of features.
• It communicates design intent more clearly than coordinate dimensions alone.
• GD&T helps ensure assembly, interchangeability, function and consistent inspection.
• Common standards include ASME Y14.5 and ISO GPS standards; requirements differ by standard and edition.
SCHEMATIC
KEY POINT
GD&T controls geometry, not just feature size.
GD&T • Geometric Dimensioning & Tolerancing
03

## Slide 4
3. Why Size Tolerances Are Not Enough
Size vs. geometry
• A hole can be within diameter limits but still be in the wrong position.
• A surface may meet a size requirement yet be bowed, twisted or tilted.
• GD&T defines how a feature relates to ideal geometry and functional datums.
• It can permit useful variation while protecting assembly function.
• Example: a bolt pattern needs both hole-size limits and positional control.
SCHEMATIC
KEY POINT
Size compliance does not guarantee location or orientation.
GD&T • Geometric Dimensioning & Tolerancing
04

## Slide 5
4. Basic Drawing Language
Terms used throughout GD&T
• Feature: a physical point, line, surface, hole, slot or derived axis/plane.
• Nominal/true geometry: the theoretically exact shape or location.
• Actual geometry: the manufactured feature, which varies within permitted limits.
• Tolerance zone: the region within which the controlled feature must lie.
• Basic dimensions: theoretically exact dimensions, commonly boxed on drawings.
SCHEMATIC
KEY POINT
Basic dimensions locate the ideal zone; the geometric tolerance defines its size.
GD&T • Geometric Dimensioning & Tolerancing
05

## Slide 6
5. GD&T Control Families
Five commonly taught control families
• Form: straightness, flatness, circularity and cylindricity.
• Orientation: parallelism, perpendicularity and angularity.
• Location: position; some standards also define concentricity and symmetry.
• Profile: profile of a line and profile of a surface.
• Runout: circular runout and total runout.
SCHEMATIC
Axis
KEY POINT
Choose the control based on functional intent.
GD&T • Geometric Dimensioning & Tolerancing
06

## Slide 7
6. How to Read a Feature Control Frame
Feature Control Frame (FCF)
• First compartment: geometric characteristic symbol.
• Next compartment: tolerance value, sometimes preceded by diameter symbol.
• Material-condition modifier may follow the tolerance value: Ⓜ MMC or Ⓛ LMC; no modifier commonly means RFS under ASME practice.
• Datum compartments identify the referenced datum features in order.
• Read the complete frame together with the feature, dimensions and notes.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
Symbol + tolerance zone + modifiers + datum references.
GD&T • Geometric Dimensioning & Tolerancing
07

## Slide 8
7. Datums and Datum Features
Reference framework
• A datum is a theoretically exact reference derived from a real datum feature.
• A datum feature is the physical feature identified on the part, such as a face, hole or cylinder.
• Datum simulators represent ideal planes, pins or other perfect references during setup/inspection.
• Datum symbols are attached to the feature outline, extension line or dimension as permitted by the standard.
• Datum references constrain the part in a repeatable coordinate system.
SCHEMATIC
A
KEY POINT
A datum is ideal; a datum feature is real.
GD&T • Geometric Dimensioning & Tolerancing
08

## Slide 9
8. 3-2-1 Datum Setup Concept
Conceptual datum reference frame
• Primary datum typically constrains three degrees of freedom.
• Secondary datum typically constrains two additional degrees of freedom.
• Tertiary datum constrains the final remaining degree of freedom.
• Exact constraints depend on feature geometry and datum simulator contact.
• Use a stable, functional setup that reproduces how the part assembles or operates.
SCHEMATIC
MEASURE
KEY POINT
A 3-2-1 setup is a useful model, not a substitute for standard-specific rules.
GD&T • Geometric Dimensioning & Tolerancing
09

## Slide 10
9. Datum Order: A | B | C
Datum reference sequence
• Datum A is the primary reference; B is secondary; C is tertiary in the referenced frame.
• Order is meaningful: changing the order can change how the tolerance is evaluated.
• Primary datum establishes the first and most important orientation/constraint.
• Datum features should be selected from functional interfaces where possible.
• Do not assume every drawing needs three datums; use only those required.
SCHEMATIC
A
KEY POINT
Use functional datum selection—not simply the easiest surfaces to measure.
GD&T • Geometric Dimensioning & Tolerancing
10

## Slide 11
10. Straightness
Form control
• Controls how straight a line element or derived median line must be.
• Surface-line straightness: each considered line element must lie between two parallel lines.
• Axis/median-line straightness can use a cylindrical tolerance zone when the diameter symbol is shown.
• Straightness is a form control and does not require a datum reference.
• Check the exact application and symbol rules in the governing standard.
SCHEMATIC
KEY POINT
No datum is required for a form tolerance.
GD&T • Geometric Dimensioning & Tolerancing
11

## Slide 12
11. Flatness
Form control
• Controls all points of a surface to lie between two parallel planes.
• Flatness does not require a datum reference.
• Tolerance value is the separation between the two planes.
• Surface finish, fixture distortion and measurement strategy can affect results.
• Inspection examples: surface plate with indicator, CMM, or suitable flatness instrument.
SCHEMATIC
KEY POINT
Flatness controls the surface itself, not its orientation to a datum.
GD&T • Geometric Dimensioning & Tolerancing
12

## Slide 13
12. Circularity (Roundness)
Form control
• Controls each circular cross-section so its points lie between two concentric circles.
• It does not control the full cylinder's straightness or taper.
• It does not require a datum reference.
• Often checked with a roundness tester or suitable rotary measurement system.
• Do not confuse circularity with circular runout; runout references a datum axis.
SCHEMATIC
Axis
KEY POINT
Circularity is evaluated in individual cross-sections.
GD&T • Geometric Dimensioning & Tolerancing
13

## Slide 14
13. Cylindricity
Form control
• Controls the entire cylindrical surface between two coaxial cylinders.
• It combines requirements related to circularity, straightness and taper over the surface.
• It is a form control and does not require a datum reference.
• Measurement may require a CMM or specialized form-measuring equipment.
• Use it when the entire cylindrical form is functionally important.
SCHEMATIC
Axis
KEY POINT
Cylindricity controls the whole surface, not just one section.
GD&T • Geometric Dimensioning & Tolerancing
14

## Slide 15
14. Parallelism
Orientation control
• Controls a surface, line element or derived axis to be parallel to a datum.
• The tolerance zone may be two parallel planes or a cylindrical zone, depending on the controlled feature and symbol usage.
• Datum reference is required.
• Parallelism does not by itself control the feature's location.
• Example: a guide rail surface kept parallel to a base datum.
SCHEMATIC
KEY POINT
Parallelism controls orientation relative to a datum.
GD&T • Geometric Dimensioning & Tolerancing
15

## Slide 16
15. Perpendicularity
Orientation control
• Controls a surface, axis or center plane at 90° to a datum.
• Tolerance zone depends on whether a surface, axis or center plane is controlled.
• Datum reference is required.
• Basic dimensions may define the theoretically exact 90° relationship.
• Example: a mounting face perpendicular to a locating base.
SCHEMATIC
KEY POINT
Perpendicularity controls 90° orientation.
GD&T • Geometric Dimensioning & Tolerancing
16

## Slide 17
16. Angularity
Orientation control
• Controls a surface, axis or center plane at a specified basic angle to a datum.
• The angle is theoretically exact; the tolerance zone permits variation around that orientation.
• Datum reference is required.
• Use basic angle dimensions with the appropriate geometric tolerance.
• Example: a machined ramp held at 30° relative to a base.
SCHEMATIC
KEY POINT
Angularity is for an angle other than the 90° controlled by perpendicularity.
GD&T • Geometric Dimensioning & Tolerancing
17

## Slide 18
17. Position (True Position)
Location control
• Controls the location of a feature of size, such as a hole or pin, relative to datums.
• Often used with basic dimensions to locate hole centers or axes.
• A diametrical tolerance zone is common for axes of holes/pins.
• Datum references establish the coordinate frame; modifiers may affect the permitted variation.
• Position is widely used for bolt patterns and interchangeable assemblies.
SCHEMATIC
KEY POINT
Position is not the same as measuring X and Y deviations independently.
GD&T • Geometric Dimensioning & Tolerancing
18

## Slide 19
18. Position Tolerance Zone
Understanding the zone
• For a hole axis, a diameter symbol before the tolerance commonly indicates a cylindrical zone.
• The actual axis/derived median line must remain within the specified zone.
• Basic dimensions locate the zone theoretically exactly.
• Datum mobility and material-condition modifiers can change how the zone is established or evaluated.
• Always interpret the feature control frame, feature size and datum modifiers together.
SCHEMATIC
KEY POINT
A ⌀ tolerance defines a cylindrical zone when the standard and application specify it.
GD&T • Geometric Dimensioning & Tolerancing
19

## Slide 20
19. MMC, LMC and RFS
Material condition concepts
• MMC: maximum material condition—most material in the feature; smallest hole or largest shaft.
• LMC: least material condition—least material; largest hole or smallest shaft.
• RFS: regardless of feature size; tolerance applies independently of actual size under ASME usage.
• Material-condition modifiers are applied only where permitted by the governing standard.
• ISO GPS uses its own rules and terminology; do not mix systems without checking.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
For a hole: MMC is its smallest permitted diameter.
GD&T • Geometric Dimensioning & Tolerancing
20

## Slide 21
20. Bonus Tolerance and Virtual Condition
Calculation concept
• When a position tolerance is specified at MMC, bonus tolerance is generally gained as the feature departs from MMC.
• Hole example: bonus = actual hole size − hole MMC size.
• Virtual condition for an internal feature under common ASME MMC application: hole MMC size minus position tolerance.
• External features use the opposite size direction for virtual-condition calculation.
• These rules depend on feature type, datum modifiers and the standard; verify before release.
SCHEMATIC
KEY POINT
Bonus tolerance is not extra size tolerance; it is extra geometric tolerance.
GD&T • Geometric Dimensioning & Tolerancing
21

## Slide 22
21. Worked Example: Hole Position
Worked calculation
• Drawing: hole diameter 10.0–10.2 mm; position ⌀0.2 at MMC relative to A|B|C.
• Hole MMC = 10.0 mm. Actual measured hole = 10.1 mm.
• Bonus tolerance = 10.1 − 10.0 = 0.1 mm.
• Total allowed position tolerance = 0.2 + 0.1 = ⌀0.3 mm.
• Assumes standard-compatible MMC application and no additional datum-shift contribution.
SCHEMATIC
KEY POINT
Actual hole size increases clearance, so allowable position tolerance can increase.
GD&T • Geometric Dimensioning & Tolerancing
22

## Slide 23
22. Profile of a Line
Profile control
• Controls the shape of a line element of a surface in a specified section.
• Tolerance zone is usually two offset curves around the true profile.
• May be applied with or without datum references depending on design intent.
• Can control complex contours that are difficult to dimension with many coordinates.
• Specify the section/extent clearly when needed.
SCHEMATIC
KEY POINT
Profile can control complex geometry with one coherent requirement.
GD&T • Geometric Dimensioning & Tolerancing
23

## Slide 24
23. Profile of a Surface
Profile control
• Controls the entire surface relative to a true profile.
• Tolerance zone is typically two offset surfaces surrounding the theoretically exact surface.
• Can control form, orientation and location depending on datum references and specification.
• Often used for castings, moulded parts, airfoils, ergonomic surfaces and complex machined contours.
• Inspect using CMM, scanning, templates or dedicated fixtures as appropriate.
SCHEMATIC
KEY POINT
Datum references determine how the profile is located and oriented.
GD&T • Geometric Dimensioning & Tolerancing
24

## Slide 25
24. Circular Runout
Runout control
• Controls variation of a surface during one full rotation about a datum axis.
• Measured at each circular cross-section while the part rotates.
• Combines effects of surface form and eccentricity relative to the datum axis.
• Requires a datum axis, typically established from a bearing journal or other functional cylinder.
• Often inspected with a dial indicator and suitable rotary setup.
SCHEMATIC
Axis
KEY POINT
Circular runout is checked section by section.
GD&T • Geometric Dimensioning & Tolerancing
25

## Slide 26
25. Total Runout
Runout control
• Controls variation over the full surface while rotating the part about a datum axis.
• Indicator traverses along the surface as the part rotates.
• Controls cumulative effects including form, alignment and surface variation relative to the axis.
• Requires a datum axis and a suitable measurement setup.
• Common for shafts, spindles, sealing surfaces and rotating components.
SCHEMATIC
Axis
KEY POINT
Total runout evaluates the whole controlled surface.
GD&T • Geometric Dimensioning & Tolerancing
26

## Slide 27
26. Concentricity and Symmetry: Caution
Legacy drawing awareness
• These controls are found in some editions/standards and may be treated differently across systems.
• ASME Y14.5-2018 removed concentricity and symmetry as geometric controls; legacy drawings may still use them.
• Many functional applications can be better controlled with position, runout or profile.
• Do not silently reinterpret legacy symbols—confirm the drawing standard and engineering authority.
• ISO GPS terminology and rules are not identical to ASME.
SCHEMATIC
Axis
KEY POINT
Always identify the applicable standard and edition.
GD&T • Geometric Dimensioning & Tolerancing
27

## Slide 28
27. Projected Tolerance Zone
Special application
• A projected tolerance zone extends beyond the part surface by a specified height.
• Useful when a fastener or pin must remain perpendicular over its projecting length.
• Often applied to position of holes for studs, dowels or threaded fasteners.
• Projection height is specified with the applicable symbol and value.
• Inspection should represent the functional projecting element.
SCHEMATIC
KEY POINT
Use when alignment matters beyond the surface of the part.
GD&T • Geometric Dimensioning & Tolerancing
28

## Slide 29
28. Tangent Plane and Unequally Disposed Profile
Advanced interpretation
• Tangent-plane modifier can define a perfect plane tangent to high points of a surface where permitted.
• Unequally disposed profile allocates different portions of a profile tolerance zone on each side of true profile.
• These controls address specific functional requirements and are standard-dependent.
• Do not assume a profile zone is equally split if a modifier says otherwise.
• Read all modifiers and notes before inspection.
SCHEMATIC
KEY POINT
Modifiers change how the tolerance zone is positioned or evaluated.
GD&T • Geometric Dimensioning & Tolerancing
29

## Slide 30
29. Free State and Flexible Parts
Special conditions
• Flexible, non-rigid parts may deform under their own weight or inspection forces.
• Free-state requirements specify evaluation without externally applied restraint, when invoked.
• Restrained-condition requirements define a fixture or loading state for inspection.
• Drawings must clearly state the applicable condition and any force/fixture details.
• Examples include thin sheet metal, rubber seals and plastic covers.
SCHEMATIC
MEASURE
KEY POINT
Inspect flexible parts in the condition specified by the drawing.
GD&T • Geometric Dimensioning & Tolerancing
30

## Slide 31
30. Common GD&T Symbols: Quick Reference
Symbol overview
• Straightness — line; flatness — parallelogram; circularity — circle; cylindricity — circle between parallel lines.
• Profile of line — arc/profile symbol; profile of surface — profile symbol with added line.
• Parallelism — parallel lines; perpendicularity — right-angle symbol; angularity — angle symbol.
• Position — target/crosshair; circular runout — single runout arrow; total runout — double runout arrow.
• Symbol appearance can vary by font/rendering; use the official symbol table in the applicable standard.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
Verify exact symbols in the drawing standard; fonts may render them differently.
GD&T • Geometric Dimensioning & Tolerancing
31

## Slide 32
31. GD&T Inspection Equipment
Measurement methods
• Calipers and micrometers: verify feature size, not all geometric controls.
• Dial indicators and fixtures: useful for runout, alignment and comparative checks.
• Surface plate, height gauge and squares: support basic setup and orientation checks.
• CMM/vision/scanning systems: evaluate complex geometry and datum relationships.
• Functional gauges: fast acceptance checks when designed to the correct virtual-condition requirement.
SCHEMATIC
MEASURE
KEY POINT
Use equipment suited to the tolerance and measurement uncertainty.
GD&T • Geometric Dimensioning & Tolerancing
32

## Slide 33
32. Inspection Planning Checklist
Practical workflow
• Confirm drawing revision, units and governing GD&T standard/edition.
• Identify the controlled feature, FCF, basic dimensions, datum features and modifiers.
• Choose a datum setup that simulates functional assembly and is repeatable.
• Select equipment with adequate resolution and measurement uncertainty.
• Define sampling, temperature, cleanliness, fixturing and reporting requirements.
• Document results and resolve ambiguous or conflicting requirements with engineering.
SCHEMATIC
MEASURE
KEY POINT
Never inspect from a cropped drawing without the notes and standard.
GD&T • Geometric Dimensioning & Tolerancing
33

## Slide 34
33. Common GD&T Mistakes
Avoid these errors
• Confusing datum and datum feature.
• Treating basic dimensions as plus/minus tolerances.
• Reading a diametrical position tolerance as separate X and Y limits.
• Ignoring MMC/LMC modifiers or incorrectly calculating bonus tolerance.
• Using runout when a form control alone is intended—or vice versa.
• Mixing ASME and ISO rules without checking the specified standard.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
The full drawing specification governs acceptance.
GD&T • Geometric Dimensioning & Tolerancing
34

## Slide 35
34. Worked Example: Datum-Based Perpendicularity
Inspection example
• Requirement: a mounting face must be perpendicular to datum A within 0.05 mm.
• Set datum A on an appropriate simulator or surface plate, per the drawing setup.
• Measure the controlled face with a height gauge/indicator or CMM.
• Evaluate the full surface against the permitted pair of parallel planes oriented 90° to datum A.
• Do not judge perpendicularity only from one edge or one point.
SCHEMATIC
KEY POINT
Tolerance-zone evaluation—not a single angle reading—determines compliance.
GD&T • Geometric Dimensioning & Tolerancing
35

## Slide 36
35. Worked Example: Runout
Inspection example
• A shaft journal establishes datum axis A; a second cylindrical surface has circular runout 0.03 mm to A.
• Mount the shaft using a setup that establishes datum axis A reliably.
• Rotate one full revolution and record indicator variation at a specified cross-section.
• Total indicator reading (TIR) is the maximum minus minimum reading for that revolution.
• Acceptance depends on the specified runout control and proper setup; TIR alone is not a universal substitute for every GD&T evaluation.
SCHEMATIC
Axis
KEY POINT
The datum axis and setup are part of the requirement.
GD&T • Geometric Dimensioning & Tolerancing
36

## Slide 37
36. GD&T vs. Traditional ± Dimensioning
Comparison
• ± dimensions are intuitive for size and coordinate limits but can overconstrain patterns.
• GD&T defines functional tolerance zones and datum relationships.
• Position tolerances can better represent bolt-pattern assembly requirements.
• Profile can simplify complex contours compared with many individual coordinates.
• Use both dimensioning methods where appropriate; GD&T is not a replacement for all size dimensions.
SCHEMATIC
KEY POINT
Choose the clearest, functionally correct specification.
GD&T • Geometric Dimensioning & Tolerancing
37

## Slide 38
37. Design Review Checklist
For design engineers
• Does each control protect a real functional requirement?
• Are datum features stable, accessible and related to assembly function?
• Are basic dimensions and tolerance values complete and unambiguous?
• Are modifiers and datum material-boundary requirements intentional?
• Can the supplier inspect the requirement with a realistic method?
• Are tolerances achievable for the process, cost and measurement capability?
SCHEMATIC
A
KEY POINT
A good GD&T drawing is functional, clear and inspectable.
GD&T • Geometric Dimensioning & Tolerancing
38

## Slide 39
38. Quick Quiz
Test your understanding
• 1) Which family includes flatness and circularity?
• 2) Does flatness require a datum reference?
• 3) For a hole, what size is MMC?
• 4) What does a diameter symbol before a position tolerance commonly indicate?
• 5) What is the key difference between circular runout and total runout?
• 6) What should you check before interpreting a legacy drawing?
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
Answer key follows.
GD&T • Geometric Dimensioning & Tolerancing
39

## Slide 40
39. Quiz Answer Key
Review answers
• 1) Form.
• 2) No; flatness is a form control.
• 3) The smallest permitted hole diameter.
• 4) A cylindrical tolerance zone for the controlled axis/derived median line, when applicable.
• 5) Circular runout evaluates cross-sections; total runout evaluates the full surface during rotation.
• 6) The governing standard and edition, plus drawing notes and engineering intent.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
When uncertain, confirm interpretation with the drawing owner.
GD&T • Geometric Dimensioning & Tolerancing
40

## Slide 41
40. Final Revision & Safety Notes
Key takeaways
• Read the complete feature control frame and related dimensions.
• Identify the controlled feature and the datum reference frame.
• Understand the tolerance zone and all modifiers before measuring.
• Use the correct standard and edition; ASME Y14.5 and ISO GPS are not interchangeable.
• Use official standards for production acceptance, supplier disputes and regulated applications.
• Training deck is educational; it does not replace licensed/controlled standards or company procedures.
SCHEMATIC
⌖
⌀0.10
A
B
KEY POINT
Interpretation must follow the drawing's specified standard.
GD&T • Geometric Dimensioning & Tolerancing
41

## Slide 42
41. Further Study & Reference
Use controlled, current editions for contractual interpretation
• ASME Y14.5 — Dimensioning and Tolerancing (use the edition named on the drawing).
• ISO GPS standards — relevant standards may include ISO 1101 (geometrical tolerancing), ISO 5459 (datums), ISO 8015 (fundamentals) and related documents.
• Company drafting manual, inspection procedure, customer-specific requirements and drawing notes.
• Training recommendation: practise reading real drawings, setting datums and evaluating one control at a time.
• Important: this presentation summarizes concepts; exact symbol rules, defaults and evaluation procedures are standard- and edition-dependent.
REFERENCE / PRACTICE
⌖
⌀0.10
A
B
PRACTICE
Read the frame, identify datums, sketch the zone, plan inspection.
GD&T • Geometric Dimensioning & Tolerancing
42