## Slide 1
CAD & MANUFACTURING • ENGINEERING SERIES
INJECTION MOULD
PARTS EXPLAINED
Illustrated guide • Functions • Materials • Design checks
Understand the major components of a conventional two-plate plastic injection mould.
EDUCATIONAL EDITION | EDITABLE POWERPOINT
PARTS • PURPOSE • WORKING

## Slide 2
A mould is a system of connected components
INTRODUCTION
02
Stationary half
Sprue / runner / gate
Cavity & core
Ejector pins
Feed system
Carries molten plastic from the machine nozzle into the cavity.
Moulding area
Cavity and core create the part's external and internal geometry.
Support & ejection
Plates, guide parts and ejectors support the tool and release the part.
Schematic only — actual mould layouts vary by part, machine and tool design.

## Slide 3
1. Stationary half and moving half
MOULD STRUCTURE
03
Stationary half (front half)
Bolts to the fixed platen. Usually contains the locating ring, sprue bush and one side of the cavity.
Moving half (rear half)
Bolts to the moving platen. Often contains the core, support system and ejector mechanism.
Why it matters
• Establishes the parting line
• Aligns the cavity and core
• Opens for part removal
• Must resist injection pressure and remain aligned
Exact component arrangement depends on mould type.

## Slide 4
2. Locating ring and sprue bush
FEED SYSTEM
04
Locating ring
Centres the mould on the machine's fixed platen / nozzle axis.
Sprue bush
Provides a hardened entry path for molten plastic from the nozzle.
Design checks
• Correct locating-ring diameter
• Nozzle radius and orifice compatibility
• Good seating and sealing
• Wear-resistant material
• Easy sprue release
A mismatch between nozzle and sprue bush can cause leakage, pressure loss or damage.

## Slide 5
3. Sprue, runner and gate
FEED SYSTEM
05
Sprue
Runner
Gate
Cavity
Sprue
Main channel from nozzle into the mould.
Runner
Distributes melt toward one or more gates.
Gate
Small entrance controlling flow into the cavity; also affects packing and gate vestige.
The diagram is conceptual; runner and gate dimensions must be designed for the resin and part.

## Slide 6
4. Cavity and core
PART-FORMING COMPONENTS
06
Cavity
Forms the outside surfaces of the component.
Core
Forms internal features such as holes, recesses or the inner profile.
Design considerations
• Parting line and shut-offs
• Draft angle
• Wall thickness and radii
• Surface finish / texture
• Shrinkage and steel-safe allowance
• Cooling access and venting
Cavity/core ownership of surfaces depends on geometry and the chosen parting strategy.

## Slide 7
5. Main plates and support plates
STRUCTURE & SUPPORT
07
Cavity plate
Holds cavity inserts or contains the cavity profile.
Core plate
Holds the core or core inserts.
Support plate
Supports the core-side plate against injection load.
Clamping plates
Attach each mould half to the machine platens.
Spacer blocks
Create space for the ejector assembly to move.
Back plate / retainer
Supports inserts or retains components depending on the design.
Plate names and exact stack-up vary with two-plate, three-plate, hot-runner and specialised mould designs.

## Slide 8
6. Guide pillars and guide bushes
ALIGNMENT
08
Guide pillar
Fixed post that guides the moving half during opening and closing.
Guide bush
Precision sleeve that works with the pillar to maintain alignment.
Why alignment matters
• Protects cavity and core shut-offs
• Reduces mismatch and flash risk
• Helps repeatable mould closing
• Requires lubrication / maintenance as specified
Guide components do not replace proper machine platen alignment or adequate mould support.

## Slide 9
7. Ejector system: pins, plates and return
EJECTION
09
Ejector pins
Push the moulded part off the core after opening.
Ejector plates
Hold and move the pins together as the ejection system advances.
Other elements
• Return pins / return mechanism
• Ejector guide pins and bushes
• Ejector sleeves or blades
• Ejector stroke and stop system
Ejector layout should avoid cosmetic damage, excessive local stress and part distortion.

## Slide 10
8. Ejector types and when they are used
EJECTION
10
Ejector pin
General-purpose ejection on robust surfaces.
Ejector sleeve
Often used around round cores or bosses.
Ejector blade
Useful for narrow ribs or thin rectangular features.
Stripper plate
Pushes a larger area for more even release.
Air ejection
Can assist release where tool design permits.
Lifter / angled ejector
Can help release selected undercuts in suitable designs.
Select the ejection method based on geometry, surface requirements, draft and tooling complexity.

## Slide 11
9. Cooling channels and fittings
THERMAL CONTROL
11
Cooling channels
Carry water or another specified coolant to remove heat from the mould.
Fittings / plugs
Connect, seal or terminate each circuit; leaks must be prevented.
Cooling design checks
• Uniform cooling near cavity/core
• Balanced flow in circuits
• Leak and pressure testing
• Accessible connectors
• Avoid weak steel sections
Cooling performance strongly affects cycle time, shrinkage and warpage.

## Slide 12
10. Vents and air traps
FILLING QUALITY
12
Vent land
A shallow path lets trapped air escape while restricting melt flash.
Venting principles
• Locate near last-to-fill areas
• Keep vents clean
• Use resin-appropriate dimensions
• Avoid excessive depth that causes flash
• Review burns and short shots together
Vents are designed to release air and gases; dimensions must follow material and tooling guidance, not a universal value.

## Slide 13
11. Inserts, slides and lifters
SPECIAL FEATURES
13
Core / cavity insert
Replaceable precision component that forms selected part geometry.
Slide
Moves laterally to form or release side features and undercuts.
Lifter
Moves along an angled path to release selected internal/external undercuts.
Angle pin / cam
Mechanism that drives a slide as the mould opens or closes.
Wear plate / gib
Guides and supports slide movement under load.
Stop block / limit
Controls travel and helps prevent over-travel.
Side actions increase tooling complexity and require adequate clearance, strength, lubrication and maintenance.

## Slide 14
12. Fasteners, locating parts and seals
ASSEMBLY
14
Socket-head screws
Clamp plates and retain components. Select suitable size, grade, engagement and tightening method.
Dowel pins / keys
Locate plates and inserts accurately; prevent unwanted shift during assembly.
O-rings / seals
Seal cooling circuits or hot-runner interfaces where the design requires them.
• Use the drawing and BOM to confirm quantity, material and fit.
• Check screw length, thread engagement, clearances and service access.
• Use the specified seal material and groove design for temperature and coolant.

## Slide 15
13. Cold-runner and hot-runner systems
FEED SYSTEM OPTIONS
15
Cold runner
• Plastic in the sprue/runner solidifies each cycle
• Runner may be reprocessed only if allowed by material and quality rules
• Simpler tool concept and maintenance in many applications
• Runner mass and removal affect cycle and scrap
Hot runner
• Heated manifold/nozzles keep feed material molten
• Can reduce cold-runner waste and support multi-cavity layouts
• Higher system cost and more thermal-control requirements
• Requires careful balancing, sealing and maintenance
Neither system is universally better. Selection depends on part quality, material, production volume, budget and process capability.

## Slide 16
14. Two-plate vs three-plate mould
MOULD TYPES
16
Two-plate mould
Typically has one main parting plane. Runner and part are commonly released at the same opening plane, depending on design.
Common for straightforward layouts and many production parts.
Three-plate mould
Uses an additional plate / parting plane to separate the runner from the part or enable specific gating arrangements.
Adds complexity, opening sequence and maintenance considerations.
The mould type determines the plate stack, feed-system layout and ejection sequence.

## Slide 17
15. How to read a mould parts list (BOM)
DESIGN WORKFLOW
17
• Item number and component name
• Standard / supplier code and drawing reference
• Material grade, hardness or surface treatment
• Quantity and assembly location
• Fit, tolerance and inspection requirement
• Revision and replacement / maintenance information
Example BOM row
Item: 12
Component: Guide pillar
Material: Tooling-standard grade per drawing
Qty: 4
Fit: As specified in mould assembly drawing
Always follow the approved drawing and standard-component supplier catalogue; do not infer dimensions from a generic picture.

## Slide 18
16. Inspection and maintenance checklist
TOOL CARE
18
• Clean cavity, core, parting line and vents safely
• Inspect guide pillars, bushes and slide wear
• Check ejector pins for bending, galling or sticking
• Inspect cooling circuits for leaks, scale and flow reduction
• Check fasteners, locating features and inserts
• Record shot count, repairs and recurring defects
• Follow lockout, guarding and hot-tool procedures
• Use approved lubricants and cleaning agents
• Protect polished / textured surfaces from damage
• Dry and protect the mould before storage as specified
• Reassemble and verify movement before production
• Document maintenance and verify first-off parts

## Slide 19
17. Component-related symptoms
TROUBLESHOOTING
19
Symptom | Components / factors to inspect
Flash at parting line | Parting surfaces, alignment, clamp force, pressure profile
Part sticks on core | Draft, surface condition, shrinkage, cooling and ejection
Short shot at end of fill | Gate/runner restriction, vents, flow path, material/process
Cooling leak | Fitting, seal, plug, corrosion or damaged channel
Mismatch / step | Guide system, locating features, wear or plate alignment
Ejector whitening | Pin layout, draft, ejection force, part temperature

## Slide 20
Mould parts: quick revision
SUMMARY
20
Feed
Locating ring, sprue bush, sprue, runner, gate
Forming
Cavity, core, inserts, shut-offs, parting line
Structure
Clamping plates, cavity/core plates, support plate, spacers
Alignment
Guide pillars, guide bushes, locating features
Ejection
Ejector pins, sleeves, blades, plates, returns
Thermal / air
Cooling channels, fittings, plugs, vents
Side actions
Slides, lifters, angle pins, wear plates
Assembly
Screws, dowels, keys, seals, stop blocks

## Slide 21
Knowledge check
PRACTICE
21
• 1. Which component centres the mould on the fixed platen?
• 2. Which components form the external and internal geometry of a part?
• 3. What is the main purpose of the gate?
• 4. Which system pushes the part off the core?
• 5. Why are vents placed near last-to-fill regions?
• 6. What should you check if the part shows ejector whitening?
Answer key
1. Locating ring
2. Cavity and core
3. Controls entry of melt into cavity
4. Ejector system
5. To let trapped air escape
6. Draft, ejection force, pin layout and part temperature

## Slide 22
CAD & MANUFACTURING • ENGINEERING LEARNING SERIES
KNOW EVERY PART.
UNDERSTAND THE MOULD.
Injection Mould Parts Explained — Illustrated PPT
• Illustrated component diagrams
• Clear functions and design checks
• Practical troubleshooting and revision questions
ADD YOUR LOGO • BRAND NAME • CONTACT DETAILS
Technical diagrams are schematic and not to scale. Verify all production designs against approved drawings.