## Slide 1
FORMULA HANDBOOK + PRACTICAL EXAMPLES
MECHANICAL ENGINEERING
Calculations: Basic to Advanced
A practical reference for design, manufacturing, machine elements, fluids, thermodynamics, and engineering problem-solving.
LEARN THE FORMULA • CHECK THE UNITS • VERIFY THE DESIGN
01

## Slide 2
How to use this calculation handbook
Formulas are starting points; use the applicable standard and design criteria
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
02
1. Identify
List known values, unknowns, assumptions and boundary conditions.
2. Convert units
Use one consistent unit system before substituting values.
3. Calculate + check
Show the equation, substitute values and check dimensions.
• Separate nominal load from dynamic, shock and safety factors.
• Use actual material properties, operating conditions and manufacturer data.
• For safety-critical parts, verify with applicable codes, standards, testing and qualified engineering review.

## Slide 3
Formula map
Major mechanical engineering calculation areas
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
03
Math + units
Algebra, geometry, trigonometry, unit conversions
Statics + strength
Forces, moments, stress, strain, deflection
Machine design
Shafts, keys, bolts, bearings, springs
Motion + power
Speed, torque, gears, belts, power
Fluids + thermal
Pressure, flow, heat, thermodynamics
Manufacturing
Fits, tolerances, machining, sheet metal

## Slide 4
MODULE 01
Units, dimensions and geometry
Build a reliable foundation: convert units first and keep dimensions consistent.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
04

## Slide 5
1.1 Essential unit conversions
Common SI and workshop conversions
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
05
• Length: 1 m = 1000 mm; 1 inch = 25.4 mm.
• Area: 1 m² = 1,000,000 mm²; 1 cm² = 100 mm².
• Volume: 1 m³ = 1000 L; 1 L = 10⁶ mm³.
• Force: 1 kN = 1000 N; mass and force are not the same quantity.
• Pressure: 1 MPa = 1 N/mm²; 1 bar = 0.1 MPa = 100 kPa.
• Power: 1 kW = 1000 W; torque: N·m; stress: Pa or MPa.
Always write units beside values. Do not mix mm with m or bar with Pa in one equation.

## Slide 6
1.2 Geometry formulas
Useful for plates, shafts, cylinders, tanks and machined parts
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
06
Rectangle
Area: A = L × W Perimeter: P = 2(L + W)
Circle
Area: A = πD²/4 Circumference: C = πD
Cylinder
Volume: V = πD²L/4 Lateral area: A = πDL
Annulus / tube
Area: A = π(Do² − Di²)/4
Sphere
Volume: V = πD³/6 Surface area: A = πD²
Right triangle
a² + b² = c² sin θ = opposite / hypotenuse

## Slide 7
1.3 Worked example: plate volume and mass
Illustrative values only; use actual material density
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
07
• Plate dimensions: 200 × 100 × 10 mm.
• Volume: V = 200 × 100 × 10 = 200,000 mm³ = 0.0002 m³.
• Assume steel density 7850 kg/m³.
• Mass: m = ρV = 7850 × 0.0002 = 1.57 kg.
• If holes, pockets or cut-outs exist, subtract their volumes before calculating mass.
Check: density in kg/m³ × volume in m³ gives mass in kg.

## Slide 8
MODULE 02
Statics and force calculations
Calculate forces and moments before sizing structural or machine components.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
08

## Slide 9
2.1 Force, weight and resultant
Core equations
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
09
Weight
W = m g Use g ≈ 9.81 m/s² near Earth's surface.
Newton's second law
F = m a Net force produces acceleration.
Inclined plane
Component parallel: mg sin θ Normal component: mg cos θ
• For multiple forces, resolve each into x and y components.
• ΣFx = m ax; ΣFy = m ay. For static equilibrium, both sums are zero.
• Use vector directions consistently; a negative result indicates the opposite assumed direction.

## Slide 10
2.2 Moment, couple and equilibrium
Moment depends on force and perpendicular distance
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
10
• Moment magnitude: M = F × d⊥ (N·m).
• Equilibrium of a rigid body: ΣFx = 0, ΣFy = 0, ΣM = 0 for planar statics.
• Example: 200 N applied perpendicular to a lever at 0.30 m gives M = 200 × 0.30 = 60 N·m.
• For an angled force, use the perpendicular component or M = rF sin θ.
• Choose a moment center that eliminates unknown forces where possible.

## Slide 11
2.3 Friction and inclined loads
Simplified dry-friction model
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
11
Friction limit
Ff ≤ μs N (static) Ff = μk N (sliding model)
Normal force
On a simple incline: N = mg cos θ, if no other normal loads.
Caution
Real friction varies with material, lubrication, contamination, temperature and wear.
Example: μ = 0.20 and N = 500 N → friction limit ≈ 100 N under the stated simplified model.
Do not use a guessed friction coefficient for safety-critical clamps, brakes or lifting systems.

## Slide 12
2.4 Worked example: cylinder force
Theoretical force; real output is reduced by friction and operating losses
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
12
• Assume bore D = 25 mm and gauge pressure p = 5 bar = 0.5 N/mm².
• Cap-end area: A = πD²/4 = π × 25²/4 ≈ 490.9 mm².
• Extension force: F = pA = 0.5 × 490.9 ≈ 245 N.
• Equivalent mass-force ≈ 245/9.81 ≈ 25.0 kgf (not 25 kg of guaranteed safe payload).
• Rod-side retraction force is lower: F = p × (bore area − rod area).
Always check pressure at the cylinder, rod diameter, mounting, side load, speed and safety factor.

## Slide 13
MODULE 03
Strength of materials
Understand stress, strain, bending, torsion and deflection.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
13

## Slide 14
3.1 Stress and strain
Basic axial loading relationships
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
14
Normal stress
σ = F/A Units: Pa or N/mm² (MPa)
Normal strain
ε = ΔL/L Dimensionless
Hooke's law
σ = E ε Within the linear-elastic range.
• Tension and compression use the same magnitude equation but different sign conventions.
• Use the net load-bearing area, not necessarily the outside envelope area.
• Material yield strength, ultimate strength and allowable design stress are different values.

## Slide 15
3.2 Worked example: axial stress
Simple uniform bar in axial loading
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
15
• Given: tensile force F = 10,000 N; cross-section A = 200 mm².
• Average stress: σ = F/A = 10,000/200 = 50 N/mm² = 50 MPa.
• If length L = 500 mm and E = 200,000 MPa, extension ΔL = FL/(AE).
• ΔL = 10,000 × 500 / (200 × 200,000) = 0.125 mm.
• Assumptions: uniform section, centered load, linear-elastic material and small deformation.

## Slide 16
3.3 Bending stress and section properties
For elementary beam theory under appropriate assumptions
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
16
Bending stress
σ = My/I M = bending moment; y = distance from neutral axis.
Second moment
Rectangle: I = b h³/12 Bending axis matters.
Section modulus
Z = I/c; then σmax = M/Z.
• Use consistent units: N·mm with mm⁴ gives stress in N/mm².
• For a simply supported beam with a central point load P: Mmax = PL/4.
• For a uniformly distributed load w over span L: Mmax = wL²/8, when load is over the full span.

## Slide 17
3.4 Beam deflection
Common formulas for idealized, prismatic beams
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
17
Simply supported, center point load
Maximum deflection: δmax = PL³/(48EI)
Cantilever, end point load
End deflection: δ = PL³/(3EI)
• E = Young's modulus; I = second moment of area about the bending axis.
• Deflection depends strongly on span: it scales with L³ in these cases.
• Confirm supports, load location, shear effects, self-weight and allowable deflection for the real design.

## Slide 18
3.5 Torsion in circular shafts
Useful for rotating shafts and torque transmission
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
18
Maximum shear stress
τmax = Tc/J
Solid round shaft
J = πd⁴/32
Hollow round shaft
J = π(Do⁴ − Di⁴)/32
T = torque, c = outer radius, J = polar second moment of area.
For circular shafts in elastic torsion: angle of twist θ = TL/(JG), where G is shear modulus.

## Slide 19
MODULE 04
Machine design calculations
Translate loads into preliminary sizes for shafts, fasteners, bearings and springs.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
19

## Slide 20
4.1 Power, speed and torque
A core relationship for motors, gearboxes and drives
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
20
Rotational power
P = Tω = 2πNT/60 N in rpm; T in N·m; P in W.
Torque from power
T (N·m) = 9550 × P(kW)/N(rpm)
Linear power
P = Fv (W), for force aligned with velocity.
Example: 2.2 kW at 1450 rpm → T ≈ 9550 × 2.2 / 1450 = 14.5 N·m.
This is ideal shaft torque before losses; confirm motor rating, service factor and duty.

## Slide 21
4.2 Shaft sizing overview
Combined bending and torsion require an appropriate failure criterion
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
21
• Solid shaft polar moment: J = πd⁴/32; bending I = πd⁴/64.
• Pure torsion estimate: τmax = 16T/(πd³) for a solid circular shaft.
• Pure bending estimate: σmax = 32M/(πd³) for a solid circular shaft.
• Real shafts may include keyways, shoulders, fatigue, stress concentration, axial load and shock.
• Check deflection, critical speed, bearing fits, surface finish, corrosion and applicable design factors.
Do not release a shaft using a single stress formula alone.

## Slide 22
4.3 Bolts and fasteners
Preliminary load checks — not a substitute for joint design standards
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
22
Average tensile stress
σ = F/Aₜ Use tensile stress area for threaded fasteners.
Average shear stress
τ = V/A Account for number of shear planes and load distribution.
Bearing stress
p ≈ F/(t d) Check plate bearing, edge distance and tear-out.
• Bolt preload, joint separation, slip, fatigue, prying and thread engagement can govern.
• Do not assume load divides equally unless geometry and stiffness justify it.
• For lifting, pressure systems or safety-critical joints, use approved standards and qualified review.

## Slide 23
4.4 Bearings, gears and belts
Selection requires operating data and manufacturer ratings
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
23
• Basic bearing life estimate: L10 (million rev) = (C/P)^p; p = 3 for ball bearings, 10/3 for roller bearings.
• Life in hours: L10h = 10⁶ L10 / (60 n), where n is rpm.
• Gear ratio (simple pair): i = driver speed / driven speed = driven tooth count / driver tooth count.
• Approximate belt speed: v = π D n / 60, if D is pulley pitch diameter in metres and n is rpm.
• Check lubrication, contamination, misalignment, shock, temperature, belt tension and manufacturer limits.

## Slide 24
4.5 Springs and safety factors
Use load-deflection data and appropriate standards
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
24
Linear spring
F = kx k in N/mm or N/m; match units to x.
Nominal factor
FoS = strength criterion / calculated demand
Design judgment
Choose criteria and factors based on failure mode, uncertainty, duty and standards.
A single factor of safety does not address every failure mode. Fatigue, buckling, wear and instability may need separate checks.

## Slide 25
MODULE 05
Pneumatics and hydraulics
Estimate actuator forces and flow, then verify the real circuit and hardware.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
25

## Slide 26
5.1 Pressure, force and piston area
Core actuator equations
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
26
Pressure
p = F/A 1 MPa = 1 N/mm².
Piston area
A = πD²/4
Theoretical cylinder force
F = pA (extension) F = p(A − Arod) (retraction)
• Use pressure at the actuator while moving, not just the compressor setting.
• Subtract rod area for retraction; account for seal friction and back pressure.
• Side loads, buckling, mounting and impact can govern before force capacity does.

## Slide 27
5.2 Cylinder speed and air consumption
Simplified sizing relationships
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
27
• Average piston speed: v = stroke / time.
• Geometric swept volume per stroke: V = A × stroke.
• Approximate free-air demand per cycle requires converting cylinder volume to reference pressure and temperature, then accounting for extension/retraction and cycle frequency.
• Flow demand depends on stroke, bore, rod, cycle rate, supply pressure, tubing, valve flow capacity and leakage.
• Use the cylinder and valve manufacturer's sizing charts; include cushioning and duty-cycle limits.
Pneumatic calculations are estimates; verify force and speed at the actual operating point.

## Slide 28
5.3 Hydraulic power
Ideal fluid power relationship
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
28
Hydraulic power
P(kW) = p(bar) × Q(L/min) / 600
Example
100 bar × 12 L/min / 600 = 2.0 kW ideal
Real input power
Pinput > Pfluid due to pump, motor and circuit losses.
Use rated pressure, flow, temperature, relief-valve setting and component ratings; pressure can remain hazardous after shutdown.

## Slide 29
MODULE 06
Fluid mechanics and flow
Calculate pressure, flow and head with clear assumptions.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
29

## Slide 30
6.1 Flow rate and velocity
Continuity equation
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
30
Volumetric flow
Q = A v
Circular pipe area
A = πD²/4
Worked example
D = 20 mm; v = 1.5 m/s → Q ≈ 0.000471 m³/s = 28.3 L/min
• Use internal diameter, not nominal outside diameter.
• For compressible gas, density changes with pressure and temperature; simple incompressible continuity may be insufficient.
• Check Reynolds number and pressure losses before selecting a pump or valve.

## Slide 31
6.2 Pressure, head and Bernoulli
Ideal energy equation for steady flow along a streamline
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
31
p/(ρg) + v²/(2g) + z = constant (ideal form)
• Hydrostatic pressure: p = ρ g h for a static fluid column.
• Pressure head: h = p/(ρg).
• Real systems require head-loss terms for friction, fittings, valves and changes in geometry.
• Pump selection must consider the system curve, required flow, elevation and efficiency.

## Slide 32
6.3 Reynolds number and pipe losses
Check flow regime and friction before sizing a line
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
32
Reynolds number
Re = ρvD/μ = vD/ν
Darcy–Weisbach
Δp = f (L/D) (ρv²/2)
Minor losses
Δp = K (ρv²/2)
Use a consistent friction-factor definition: Darcy friction factor is four times the Fanning factor.

## Slide 33
MODULE 07
Thermodynamics and heat transfer
Use energy balances and temperature-dependent material data.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
33

## Slide 34
7.1 Heat and temperature change
Sensible heat relationship
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
34
Q = m cₚ ΔT
• Q = heat energy (J); m = mass (kg); cp = specific heat capacity (J/kg·K).
• Example: heat 2 kg of water by 20 K, using cp ≈ 4180 J/kg·K.
• Q = 2 × 4180 × 20 = 167,200 J ≈ 167 kJ.
• This excludes phase changes, vessel heating and environmental losses.

## Slide 35
7.2 Conduction, convection and radiation
Heat transfer modes
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
35
Conduction
Q̇ = k A ΔT / L (simple 1D steady slab)
Convection
Q̇ = h A (Ts − T∞)
Radiation
Q̇ = ε σSB A (Ts⁴ − Tsur⁴)
Use absolute temperature in kelvin for radiation; properties and boundary conditions matter.

## Slide 36
7.3 Thermodynamic relationships
Useful idealized gas and energy equations
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
36
• Ideal gas: pV = mRT, using absolute pressure and temperature.
• First law for a closed system: ΔU = Q − W, with work sign convention stated.
• Thermal expansion: ΔL = α L ΔT for a uniform member in free expansion.
• Efficiency: η = useful output / input, on a consistent energy or power basis.
• Do not use ideal-gas or constant-property assumptions outside their valid range without checking.

## Slide 37
MODULE 08
Manufacturing and quality calculations
Connect engineering drawings to tolerances, machining and production checks.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
37

## Slide 38
8.1 Fits and tolerances
Understand size limits before selecting a fit
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
38
Tolerance
Tolerance = maximum limit − minimum limit
Clearance
Clearance = hole size − shaft size (positive = gap)
Interference
Interference = shaft size − hole size (positive = overlap)
Select fits from a recognized fit system and functional requirement; do not choose a fit from nominal size alone.

## Slide 39
8.2 Cutting speed, rpm and feed
Common machining estimates
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
39
N (rpm) = 1000 Vc / (π D)
Vc in m/min; D in mm.
Turning feed rate: Vf (mm/min) = f (mm/rev) × N (rpm)
• Example: Vc = 100 m/min, D = 20 mm → N ≈ 1592 rpm before machine-limit adjustment.
• Actual cutting data depends on material, tool grade, coating, rigidity, coolant and operation.
• For milling, feed per minute commonly uses feed per tooth × number of teeth × spindle rpm.

## Slide 40
8.3 Sheet metal and manufacturing checks
Formula-based estimates need process-specific validation
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
40
• Flat pattern and bend allowance depend on inside radius, thickness, bend angle, material and K-factor.
• Approximate bend allowance: BA = θ(R + Kt), with θ in radians under the stated convention.
• Mass = density × net volume; subtract holes and cut-outs.
• Production capability should be checked against machine, tooling, material batch and inspection method.
• Use the shop's validated bend tables, cutting data and process standards for released work.

## Slide 41
MODULE 09
Electrical basics, vibration and reliability
Understand common calculations encountered in machine design and maintenance.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
41

## Slide 42
9.1 Electrical power for mechanical engineers
Basic single-phase and three-phase relationships
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
42
DC / ideal resistive
P = VI = I²R = V²/R
AC single phase
Real power: P = VI cos φ
Balanced 3-phase
P = √3 VL IL cos φ
Motor input power differs from shaft output power due to efficiency and power factor.

## Slide 43
9.2 Vibration and rotating systems
Useful introductory relationships
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
43
Frequency
f = 1/T; angular frequency ω = 2πf
Centripetal acceleration
a = ω²r = v²/r
Unbalance force
F = m e ω² (simple rotating unbalance)
• Check units: ω in rad/s, radius in m, mass in kg.
• Vibration depends on forcing, natural frequency, damping, mounting and system stiffness.
• Balancing and vibration acceptance criteria should follow the applicable machine standard.

## Slide 44
9.3 Buckling and fatigue awareness
Failure modes beyond simple static stress
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
44
• Ideal Euler buckling load: Pcr = π²EI/(Le)² for a slender, ideal elastic column.
• Effective length Le depends on end conditions; real imperfections and eccentric loads reduce capacity.
• Fatigue depends on stress range, mean stress, material, surface, size, notches and environment.
• Use appropriate design methods, load spectra, standards and validation for real components.
• Do not treat ideal textbook equations as allowable working loads.

## Slide 45
MODULE 10
Worked examples and design workflow
Practice a repeatable calculation process and document every assumption.
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
45

## Slide 46
10.1 Example: convert motor torque to linear force
Idealized screw-drive relationship
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
46
• Given torque T = 10 N·m, screw lead l = 5 mm/rev = 0.005 m/rev.
• Ideal force relation: F = 2πT/l.
• Fideal = 2π × 10 / 0.005 ≈ 12,566 N.
• If screw efficiency η = 0.85, approximate output force F ≈ η × Fideal ≈ 10,681 N.
• Real capacity also depends on screw type, critical speed, buckling, bearing support, duty, alignment and manufacturer ratings.

## Slide 47
10.2 Example: estimate a simply supported beam
Central point load, ideal prismatic beam
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
47
• Given P = 500 N, span L = 1000 mm, E = 200,000 N/mm², I = 1.0 × 10⁶ mm⁴.
• Maximum moment: Mmax = PL/4 = 500 × 1000/4 = 125,000 N·mm.
• Maximum deflection: δ = PL³/(48EI).
• δ = 500 × 1000³ / (48 × 200,000 × 1.0×10⁶) ≈ 0.052 mm.
• Check the assumed I and units; the result is only for the stated ideal support and load model.

## Slide 48
10.3 Calculation sheet template
Use this structure in Excel or your engineering calculation report
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
48
Inputs
Value • unit • source • tolerance • operating range
Method
Formula • assumptions • standard • load case
Results
Calculated value • unit • allowable • margin
• Add a free-body diagram or sketch where forces and supports are involved.
• Record material grade, temperature, duty cycle, uncertainty and worst-case conditions.
• Include independent checks, reviewer, revision, date and reference documents.

## Slide 49
Calculation checklist before release
A practical review for mechanical design calculations
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
49
All inputs have units and traceable sources
Load cases include start, stop, shock and duty where relevant
Equations match the physical model and assumptions
Material properties and allowable criteria are appropriate
Units and dimensions are checked independently
Stress, deflection, stability, fatigue and wear considered as applicable
Safety factors and standards are stated
Results reviewed, documented and independently checked

## Slide 50
Practice questions
Try solving before checking the equations
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
50
Beginner
Find the mass of an aluminium block 100 × 50 × 20 mm. Use a stated density assumption.
Intermediate
A 1 kW motor runs at 1000 rpm. Estimate shaft torque.
Advanced
Estimate beam stress and deflection for a defined load, span, support and section.
For each answer, show knowns, formula, substitution, units and a reasonableness check.
Important: the worked examples are educational estimates, not certified design approvals.

## Slide 51
Recommended references
Confirm current formulas, property data and design rules using trusted references
MECHANICAL ENGINEERING CALCULATIONS • FORMULAS + WORKED EXAMPLES
51
Machine Design
Shigley's Mechanical Engineering Design or an equivalent recognized textbook.
Engineering Mechanics
Statics and mechanics of materials textbooks for derivations and assumptions.
Standards
Use applicable ISO, ASME, BIS and industry standards for actual design work.
Manufacturer data
Use current catalogs for bearings, cylinders, fasteners, gearboxes, valves and motors.
Always check edition, local requirements and the exact operating conditions.

## Slide 52
YOUR ENGINEERING WORKFLOW
Define the load. Choose the model. Calculate. Verify.
Good engineering is not only getting a number — it is knowing what the number means, what assumptions support it, and what could make it wrong.
FORMULAS • UNITS • ASSUMPTIONS • VALIDATION
52