## Slide 1
MECHANICAL ENGINEERING • TECHNICAL INTERVIEW
MEASURING INSTRUMENTS COMPLETE STUDY GUIDE
Instrument purpose, parts, working principles, least count, use, errors, calibration and interview questions.
ILLUSTRATED • PRACTICAL • INTERVIEW READY
12.45 mm
For diploma, ITI, technician, quality, production and maintenance interviews

## Slide 2
1. Measurement Fundamentals
The language of dimensional inspection
2
Measurement compares an unknown quantity with an accepted standard.
Accuracy: closeness to the reference value; precision: repeatability of readings.
Resolution is the smallest displayed/readable increment; it is not the same as accuracy.
Least count is the smallest value an instrument can resolve by its scale/design.
Tolerance is the permitted dimensional variation; uncertainty describes doubt in a result.
Always record the value with units and the instrument identification when required.
Outside • inside • depth
INSTRUMENT SCHEMATIC
Interview tip: Be able to explain accuracy, precision, resolution, least count and tolerance distinctly.

## Slide 3
2. Choosing the Right Instrument
Match instrument, feature and tolerance
3
Steel rule: quick approximate length checks.
Vernier caliper: external, internal and depth dimensions across a useful range.
Micrometer: accurate outside diameter or thickness measurements.
Bore gauge: internal diameter variation; often used with a setting standard.
Dial indicator: comparative displacement, runout and alignment checks.
Use an instrument whose range and uncertainty suit the tolerance being inspected.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 4
3. Steel Rule
Simple length measurement
4
Purpose: quick measurement and layout for general workshop work.
Common graduations: millimetres and sometimes half-millimetres or inches.
Working principle: align the zero/reference edge and read the scale at the feature.
Keep the rule straight, clean and close to the measured line.
Limitations: lower precision than calipers or micrometers; damaged zero edges cause error.
Graduated steel rule
Read from zero; avoid parallax
INSTRUMENT SCHEMATIC
Interview tip: Avoid parallax by looking squarely at the scale.

## Slide 5
4. Vernier Caliper
External, internal and depth measurement
5
Main parts: main scale, vernier scale, fixed jaw, sliding jaw, depth rod and lock.
External jaws measure outside dimensions; inside jaws measure internal dimensions.
Depth rod measures hole or step depth when correctly seated.
Traditional least count = one main-scale division − one vernier-scale division.
Reading = main-scale reading + (coinciding vernier division × least count).
Close the jaws gently and check zero error before measuring.
Outside • inside • depth
INSTRUMENT SCHEMATIC
Interview tip: For a typical 0.02 mm least-count caliper, verify the actual instrument marking.

## Slide 6
5. Digital Caliper
Electronic display and practical checks
6
Uses a sensor and digital display to show the measured dimension.
Common functions: mm/inch conversion, zero/set and relative measurement.
Check battery condition, jaw cleanliness and zero reading before use.
Press zero only when the reference position is correct for the measurement.
Do not use the jaws as a clamp or expose the tool to chips, coolant or impact beyond its rating.
Digital display resolution does not guarantee equal measurement accuracy.
12.45
Outside • inside • depth
INSTRUMENT SCHEMATIC

## Slide 7
6. Outside Micrometer
Precision outside diameter and thickness
7
Main parts: frame, anvil, spindle, sleeve/barrel, thimble, ratchet and lock.
Spindle advances by a precision screw as the thimble rotates.
Read the sleeve scale and thimble scale; add them using the instrument’s scale convention.
Use the ratchet/friction device for consistent measuring force.
Check zero at the closed position and use a setting standard for larger ranges.
Keep measuring faces clean and avoid heating the tool with prolonged hand contact.
Measure outside diameter or thickness
INSTRUMENT SCHEMATIC
Interview tip: Know the range and least count stamped on the specific micrometer.

## Slide 8
7. Inside Micrometer
Internal dimensions
8
Measures internal diameters or distances between internal surfaces.
Types include rod/tubular and two-point or three-point designs.
Use the correct extension rods and setting method for the range.
Align the instrument with the bore axis; avoid tilt and excessive force.
Take readings at more than one depth and direction when checking bore geometry.
Set or verify against a ring gauge or other suitable standard when required.
Measure internal dimensions
INSTRUMENT SCHEMATIC

## Slide 9
8. Depth Gauge
Depth of holes, slots and steps
9
Base sits on a clean reference surface while the blade or rod enters the feature.
Depth micrometers provide fine adjustment; calipers may use an integral depth rod.
Ensure the base bridges the feature correctly and does not rock.
Remove burrs and chips from both the reference surface and measured feature.
Check zero on a suitable flat reference surface before use.
Do not confuse depth from the top face with depth from another datum.
Base rests on reference surface
INSTRUMENT SCHEMATIC

## Slide 10
9. Height Gauge
Height measurement and marking-out
10
Usually used on a surface plate with a scriber or measuring probe.
Measures heights from a datum and can mark lines at specified heights.
Digital, dial and vernier versions are available.
Clean the surface plate and gauge base; move the instrument without lifting it unintentionally.
Use a suitable probe and keep the column aligned.
Accuracy depends on setup, reference flatness, cleanliness and operator technique.
Height measurement from datum
INSTRUMENT SCHEMATIC

## Slide 11
10. Dial Indicator / Dial Test Indicator
Comparative measurement and alignment
11
Shows small movement of a contact point using a dial or electronic display.
Applications: shaft runout, flatness comparison, alignment, parallelism and setup checks.
Mount rigidly on a suitable stand; avoid loose magnetic bases or flexible fixtures.
Preload the contact within the specified range and align the probe appropriately.
Zero against a reference, then compare changes rather than treating every reading as an absolute dimension.
Do not exceed travel limits or force the plunger sideways.
Dial display
Check zero and movement before use
INSTRUMENT SCHEMATIC

## Slide 12
11. Bore Gauge
Internal diameter comparison
12
Common dial bore gauges compare a bore with a known setting dimension.
Set the gauge using a ring gauge or a micrometer setting arrangement.
Rock gently through the bore to find the reversal point, following the gauge design.
Take readings at several depths and orientations to assess taper and out-of-roundness.
Clean anvils/contact points and verify the setting before measurement.
Confirm whether the instrument displays deviation from nominal or a direct value.
Bore measurement
Check zero and movement before use
INSTRUMENT SCHEMATIC

## Slide 13
12. Feeler Gauge
Checking small clearances
13
Consists of thin leaves with known thicknesses.
Used for spark-plug gaps, valve clearances, machine gaps and fit-up checks where specified.
Select the leaf or combination that fits with the specified light drag.
Keep leaves clean and flat; do not force them into a gap.
Read the marked thickness and use combinations only as permitted by the procedure.
Use the specified temperature and setup conditions for critical clearances.
1
2
3
4
5
6
Thin thickness leaves
INSTRUMENT SCHEMATIC

## Slide 14
13. Thread Pitch Gauge
Identify thread pitch
14
Leaves have profiles matched to standard thread pitches.
Select the leaf that seats correctly across several thread crests without visible gaps.
Metric pitch is measured as distance between adjacent thread crests in millimetres.
Pitch gauge helps identify pitch; it does not fully verify thread diameter or tolerance class.
Use thread plug/ring gauges or specified measuring methods for acceptance inspection.
Confirm thread standard and form before selecting a gauge.
1
2
3
4
5
6
Thread pitch leaves
INSTRUMENT SCHEMATIC

## Slide 15
14. Radius Gauge
Concave and convex radii
15
Contains leaves with known radius profiles.
Use concave or convex leaf according to the part surface.
Hold against a clean profile and inspect for gaps under suitable lighting.
Useful for quick checks of fillets and rounded edges.
Not a substitute for a calibrated profile projector or CMM when tighter verification is required.
Choose the radius range and units appropriate to the drawing.
1
2
3
4
5
6
Concave / convex radius leaves
INSTRUMENT SCHEMATIC

## Slide 16
15. Slip Gauges / Gauge Blocks
Precision length standards
16
Precision blocks provide known lengths for setting and calibration tasks.
Blocks can be wrung together using clean, controlled technique where permitted.
Used to set micrometers, height gauges, comparators and sine-bar setups.
Protect blocks from corrosion, scratches and temperature changes.
Handle with clean hands or suitable gloves as required by the quality system.
Return blocks to their case after use and follow calibration/traceability rules.
Precision length standards
INSTRUMENT SCHEMATIC

## Slide 17
16. Surface Plate & Straight Edge
Reference surfaces for inspection
17
Surface plate provides a stable reference plane for layout and measurement.
Straight edge checks straightness or surface variation by an appropriate method.
Keep surfaces free of burrs, chips, dust and oil films that could affect readings.
Do not use a surface plate as a workbench or hammering surface.
Check calibration status and support conditions.
Granite and cast-iron plates have different handling and maintenance considerations.
Stable datum for inspection
INSTRUMENT SCHEMATIC

## Slide 18
17. Sine Bar
Precision angle setting
18
Uses known roller-centre distance and slip-gauge height to establish an angle.
Relation: sin θ = height difference / roller centre distance.
Example: for 100 mm centre distance and 25 mm height, θ = sin⁻¹(0.25) ≈ 14.48°.
Use a stable surface plate and appropriate gauge blocks.
Small height errors can cause angle error, especially at larger angles.
Confirm sine-bar length and the intended reference geometry.
Angle set-up with slip gauges
INSTRUMENT SCHEMATIC

## Slide 19
18. Surface Roughness Tester
Surface texture assessment
19
Measures or compares surface texture parameters such as Ra when configured for them.
Stylus instruments trace a surface over a specified evaluation length.
Set cutoff, filter, measurement direction and parameter according to the drawing/standard.
Measure perpendicular to the dominant lay where required by the method.
Keep the stylus and workpiece clean; avoid edges and damaged areas unless specified.
Ra alone does not describe every aspect of surface texture.
Surface texture comparator / tester
INSTRUMENT SCHEMATIC

## Slide 20
19. Tachometer & Stroboscope
Rotational speed measurement
20
Tachometer measures rotational speed, often in revolutions per minute (rpm).
Contact tachometers need safe, suitable contact; non-contact models may use reflective tape or optical sensing.
Stroboscope flashes at a controlled frequency to make periodic motion appear stationary.
Keep clear of rotating shafts, belts and chucks; follow machine safety rules.
Check units and whether the instrument reports rpm, rps or frequency.
Reflections, missed pulses and harmonics can cause incorrect readings.
RPM
1250
INSTRUMENT SCHEMATIC

## Slide 21
20. Temperature Instruments
Thermometer and infrared pyrometer
21
Contact thermometers measure temperature through a probe or sensor.
Infrared pyrometers estimate surface temperature from emitted infrared radiation.
Emissivity, distance-to-spot ratio, viewing angle and surface finish affect IR readings.
Shiny metal can give misleading infrared readings if settings and method are unsuitable.
Use the correct range and calibration status.
Do not touch hot parts without an approved safe method and PPE.
Temperature
INSTRUMENT SCHEMATIC

## Slide 22
21. Pressure Gauge & Flow Meter
Pressure and fluid-flow checks
22
Pressure gauge indicates pressure relative to its reference, often gauge pressure.
Check range, units, connection, pulsation and calibration status.
Flow meters measure volume or mass flow using a technology suited to the fluid and process.
Install according to manufacturer requirements, including flow direction and straight-run needs where applicable.
Depressurize safely before removing a gauge or fitting.
Never use a gauge beyond its pressure or temperature rating.
bar / MPa
INSTRUMENT SCHEMATIC

## Slide 23
22. Torque Wrench
Controlled fastener tightening
23
Applies a specified tightening torque to threaded fasteners.
Common types include click, beam, dial and electronic torque wrenches.
Select the correct torque and units from approved engineering data.
Apply force at the designated grip and use a smooth, controlled motion.
Do not use a torque wrench as a breaker bar unless designed for that purpose.
After use, store and maintain it as the manufacturer specifies; calibration matters.
Apply specified tightening torque
INSTRUMENT SCHEMATIC

## Slide 24
23. Weighing Scale & Load Measurement
Mass, load and capacity
24
Scales and load cells convert force or mass-related loading into a readable value.
Check capacity, resolution, zero and calibration status.
Place the load centrally and avoid shock loading or side loading.
Mass is expressed in kilograms; force is expressed in newtons.
Use approved lifting equipment and never stand beneath suspended loads.
Record units and any tare or zeroing operation.
12.50 kg
INSTRUMENT SCHEMATIC

## Slide 25
24. Calibration, Zero Error & Common Mistakes
How to protect measurement quality
25
Calibration compares an instrument with standards and documents its relationship to reference values.
Zero error is a non-zero indication when the instrument should indicate zero under the defined condition.
Clean the part and instrument; control burrs, temperature and measuring force.
Avoid parallax, tilted contact, poor alignment and reading the wrong scale.
Use instruments within range and check calibration status before critical inspection.
Do not adjust or repair a controlled instrument unless authorized.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 26
25. Instrument Selection by Job
Common inspection choices
26
Outside diameter: micrometer for precision; caliper for general range and convenience.
Internal bore: bore gauge or inside micrometer, set with a suitable standard.
Depth: depth micrometer, depth gauge or caliper depth rod as tolerance permits.
Runout/alignment: dial indicator with a rigid, suitable fixture.
Thread pitch: pitch gauge for identification; thread gauges for conformity.
Surface roughness: specified roughness tester or comparator method.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 27
26. Interview Questions — Basics
Practise clear, short answers
27
What is the difference between accuracy and precision?
What is least count? Is it the same as accuracy?
How do you read a vernier caliper?
What are the parts of an outside micrometer?
Why must zero error be checked?
When would you use a dial indicator instead of a caliper?
What is calibration and why is traceability important?
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 28
27. Interview Questions — Practical Scenarios
Explain the safe, systematic approach
28
A micrometer does not return to zero. What do you do?
Two instruments give different readings. How do you investigate?
A bore is within diameter limits at one end but not the other. What could this indicate?
How would you check shaft runout?
What can cause an incorrect infrared temperature reading on shiny metal?
An instrument is overdue for calibration. Can you use it for product acceptance?
How do you record and handle a nonconforming measurement?
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 29
28. Formula & Reading Revision
Remember the measurement relationships
29
Vernier reading = main-scale reading + (coinciding division × least count).
Traditional vernier least count = one main-scale division − one vernier-scale division.
Micrometer reading = sleeve/barrel reading + thimble reading, following that scale design.
Sine bar: sin θ = height difference / roller-centre distance.
Dimensional error = measured value − reference value (sign convention must be stated).
Always check instrument-specific instructions; scale layouts and resolutions differ.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 30
29. Quick Quiz
Try before checking the answers
30
Which instrument is commonly used for precise outside diameter measurement?
What does a dial indicator typically measure?
Which instrument identifies thread pitch?
What is the relation used by a sine bar?
Why can an infrared thermometer misread shiny metal?
What must be done before using an instrument for critical acceptance?
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 31
30. Quiz Answer Key
Review the reasoning, not just the words
31
Outside micrometer, when its range and accuracy suit the part.
Small displacement or change relative to a reference.
Thread pitch gauge; it does not by itself certify the full thread.
sin θ = height difference / roller-centre distance.
Emissivity and reflected radiation can affect the infrared reading.
Check cleanliness, range, zero/condition and calibration status per procedure.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 32
31. Final Checklist for the Interview
Show practical understanding
32
Identify the instrument and explain what feature it measures.
Name the key parts and describe the working principle.
Explain least count or resolution and show how to read it.
State common errors and how to avoid them.
Give one realistic workshop or inspection example.
Always mention calibration, cleanliness, safe handling and recording units.
MEASURING TOOL
Use correct range and calibrated instrument
INSTRUMENT SCHEMATIC

## Slide 33
MEASUREMENT SKILLS BUILD QUALITY
Choose the right instrument. Use it correctly. Verify the result. Record it clearly.
CLEAN • ZERO CHECK • MEASURE • VERIFY • RECORD
This PPT uses editable schematic illustrations for learning. They are not manufacturer-specific product images or calibration instructions.
33