## Slide 1
COMPLETE LEARNING ROADMAP
SOLIDWORKS
Beginner to Advanced
A practical, step-by-step guide to 3D part design, assemblies, engineering drawings and manufacturing-ready models.
TRAIN • PRACTICE • BUILD A PORTFOLIO
01

## Slide 2
What you will learn
From the first sketch to a complete engineering workflow
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
02
01 Foundations
Interface, planes, units, file types and sketching.
02 Part modeling
Extrude, revolve, cuts, patterns, fillets and design intent.
03 Assemblies
Components, mates, clearances, motion checks and BOM.
04 Drawings
Views, dimensions, tolerances, sections and annotations.
05 Advanced tools
Sheet metal, weldments, surfaces, configurations and equations.
06 Job-ready project
Design a small fixture assembly and publish a drawing pack.

## Slide 3
The learning roadmap
Recommended sequence — move forward only when you can repeat each skill independently
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
03
LEVEL 1
Interface + sketches
Weeks 1–2
LEVEL 2
Core part features
Weeks 3–4
LEVEL 3
Assemblies + drawings
Weeks 5–6
LEVEL 4
Advanced modeling
Weeks 7–8
LEVEL 5
Capstone + portfolio
Weeks 9–10
Suggested pace: 45–60 minutes per day, 5 days per week. Every lesson should include a model you build yourself.

## Slide 4
MODULE 01
Getting started with SOLIDWORKS
Understand the interface and how parametric CAD stores design intent.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
04

## Slide 5
1.1 Understand the interface
Names can vary slightly by version and workspace
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
05
FeatureManager tree
Lists sketches, features, planes and assembly components.
Graphics area
Main workspace for viewing and editing the model.
CommandManager
Tabs group tools such as Features, Sketch and Evaluate.
PropertyManager
Options and settings for the selected command.
Heads-up toolbar
Common view and display controls near the model.
Mouse controls
Rotate, zoom and pan to inspect the model.
Practice: open a new Part, identify the three default planes, then save a file as Training_Block.SLDPRT.

## Slide 6
1.2 Files, units and selection
Start every project with clear file and unit choices
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
06
• Part: .SLDPRT • Assembly: .SLDASM • Drawing: .SLDDRW
• Choose units deliberately: MMGS (millimeter, gram, second) is common in mechanical design.
• Use meaningful filenames and revision identifiers; avoid names like final_final2.
• Use Ctrl+S frequently and keep related part, assembly and drawing files together.
• Use the right mouse button for context-sensitive commands; use the shortcut bar for frequent tools.
Good habit: confirm units before entering dimensions from a drawing.

## Slide 7
MODULE 02
Sketching fundamentals
Build fully defined, editable sketches before adding 3D features.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
07

## Slide 8
2.1 Sketch workflow
A reliable sketch is the foundation of a reliable model
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
08
1
Choose a plane
Front, Top or Right
2
Draw geometry
Line, rectangle, circle, arc
3
Add relations
Horizontal, vertical, tangent, concentric
4
Dimension
Set exact sizes and positions
5
Check status
Aim for fully defined geometry
Rule of thumb: fully define the sketch when dimensions and relationships should not drift.

## Slide 9
2.2 Sketch relations and dimensions
Relations control shape; dimensions control size and position
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
09
Geometric relations
Horizontal / vertical Coincident Tangent Concentric Equal / parallel
Driving dimensions
Length, diameter, radius, angle and distance from origin.
Sketch status
Blue geometry is typically under-defined; black is typically fully defined (display may vary).
Exercise: sketch a plate outline 100 × 60 mm with four Ø8 mm holes, each 10 mm from its nearest edges. Dimension the sketch instead of estimating by eye.

## Slide 10
2.3 Common sketch tools
Practice each tool in a separate sketch before combining them
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
10
• Line / Centerline — edges, axes and construction geometry
• Corner Rectangle / Center Rectangle — plates, blocks and symmetric profiles
• Circle / Slot — holes, pins, elongated mounting holes
• Arc / Spline — curved profiles; use splines only when needed
• Trim Entities / Extend Entities — clean up intersecting geometry
• Offset Entities / Convert Entities — reuse existing geometry
• Mirror Entities — maintain symmetry and reduce duplicate sketching

## Slide 11
MODULE 03
Core 3D part modeling
Learn how sketches become features and how features form a clear model tree.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
11

## Slide 12
3.1 Essential features
Understand what each feature adds to or removes from the model
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
12
Extruded Boss/Base
Adds depth to a sketch profile.
Revolved Boss/Base
Rotates a profile around an axis.
Extruded Cut
Removes material along a direction.
Hole Wizard
Creates standard hole types and callouts.
Fillet / Chamfer
Rounds or bevels selected edges.
Pattern / Mirror
Repeats or reflects features predictably.

## Slide 13
3.2 Practice model: mounting block
Build this simple component using a feature-based workflow
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
13
Model sequence
• Sketch a centered rectangle: 80 × 50 mm.
• Extruded Boss/Base: thickness 12 mm.
• Sketch two Ø10 mm holes; position them symmetrically.
• Use Extruded Cut — Through All, or Hole Wizard when appropriate.
• Add a 2 mm fillet only where the design and manufacturing process allow.
• Rename important features: Base_Extrude, Mounting_Holes, Edge_Fillet.
Check: edit the base width and confirm the hole positions remain correct.

## Slide 14
3.3 Design intent and feature tree
A model should be easy for another engineer to edit
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
14
• Build from stable references: origin planes, axes and robust faces.
• Use symmetry, equal relations, patterns and mirror features rather than duplicate dimensions.
• Prefer fewer, meaningful features over one complicated sketch.
• Avoid unnecessary external references and fragile face-to-face dependencies.
• Rename key features; group logically and suppress optional features only when needed.
• Rebuild after edits and resolve all errors before releasing the model.

## Slide 15
MODULE 04
Intermediate & advanced part design
Expand beyond simple extrudes into complex forms, sheet metal and design automation.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
15

## Slide 16
4.1 Intermediate modeling tools
Use each tool for the geometry it is designed to create
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
16
Sweep
Move a profile along a path — e.g., a tube or handle.
Loft
Blend profiles across planes to create transitions.
Rib / Shell
Add thin supports or hollow a body with controlled wall thickness.
Configurations
Create controlled size or feature variations in one file.
Equations / Design Table
Drive dimensions from parameters and tabulated variants.
Multi-body parts
Manage multiple solid bodies in a single part file.

## Slide 17
4.2 Sheet metal essentials
Model parts with manufacturing operations in mind
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
17
• Base Flange/Tab — start from a sheet profile and thickness.
• Edge Flange, Miter Flange and Hem — create formed edges.
• Jog, Sketched Bend and Flatten — represent bends and flat patterns.
• Set thickness, bend radius and K-factor using your shop's material/process guidance.
• Inspect the flat pattern and bend lines before creating manufacturing drawings.
• Do not assume default bend allowances match every machine or material.
Practice: create an L-bracket, add two flanges, then generate its flat pattern.

## Slide 18
4.3 Weldments and structural frames
Useful for machine bases, guards, supports and fabrication frames
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
18
• Create a 2D or 3D sketch to represent the member centerlines.
• Use Structural Member with the correct profile and size.
• Use Trim/Extend to manage member intersections.
• Add end caps, gussets or plates where the design requires them.
• Create a cut list and verify member lengths, orientation and quantity.
• Confirm profile libraries and material specifications before issuing fabrication data.

## Slide 19
4.4 Surface modeling
Use surfaces for complex shapes and controlled transitions
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
19
• Surface Extrude / Revolve — create open surface geometry.
• Boundary Surface / Lofted Surface — build smooth transitions between curves.
• Trim, Knit and Extend — shape and join surface patches.
• Thicken — convert a suitable surface into a solid.
• Use curvature and zebra-stripe checks when surface quality matters.
• Repair gaps and mismatched edges before attempting to form a closed solid.

## Slide 20
MODULE 05
Assemblies and motion
Bring parts together with mates, check fit and communicate how a mechanism works.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
20

## Slide 21
5.1 Assembly workflow
A stable assembly starts with correct component references
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
21
• Create a new Assembly and insert the base component first; fix it where appropriate.
• Insert remaining components from clean, named part files.
• Apply mates: coincident, concentric, distance, angle, parallel and width as needed.
• Avoid over-defining components; inspect degrees of freedom when motion is expected.
• Use interference detection and clearance checks before release.
• Use exploded views to communicate assembly order and service access.

## Slide 22
5.2 Mates — practical examples
Choose mates based on the real mechanical relationship
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
22
Concentric
Shaft in a bearing; pin in a round hole.
Coincident
Two planar faces touching or a point on a plane.
Distance / Angle
Set a gap, travel stop or fixed orientation.
Limit Distance / Angle
Restrict motion between minimum and maximum values.
Width Mate
Center a tab or component within a slot.
Mechanical mates
Gear, rack-and-pinion, screw or hinge-style relationships when supported.

## Slide 23
5.3 Assembly quality checks
CAD fit checks support engineering review but do not replace validation
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
23
• Interference Detection — identify overlapping solids that may be unintended.
• Clearance Verification — assess gaps against defined design requirements.
• Move Component / Rotate Component — inspect expected motion and access.
• Mass Properties — check mass and center of mass using assigned materials.
• Large assemblies: simplify detail, use lightweight/resolved options thoughtfully, and suppress unused components.
• Verify fasteners, tooling access, maintenance access and cable/hose clearances.

## Slide 24
MODULE 06
Engineering drawings and GD&T
Turn 3D design data into clear, manufacturing-ready documentation.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
24

## Slide 25
6.1 Create a drawing
A drawing must communicate size, shape, tolerances and manufacturing intent
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
25
• Create Drawing from Part/Assembly and select an appropriate sheet size.
• Place standard orthographic views; add isometric view when it helps visualization.
• Use section, detail and auxiliary views where necessary.
• Add dimensions with clear references; avoid duplicate or ambiguous dimensions.
• Add center marks, centerlines, notes, material, finish and revision information.
• Use the required projection method and company drawing template.

## Slide 26
6.2 Tolerances and GD&T
Apply tolerances based on function, process capability and inspection method
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
26
Size tolerances
Limits, plus/minus tolerances and fits for shafts and holes.
Datums
Reference features that establish how a part is located and inspected.
Geometric controls
Position, flatness, perpendicularity, parallelism, profile and runout.
• Use the drawing standard required by your organization (e.g., ASME or ISO); do not mix rules casually.
• Tolerance only what is functionally necessary — tighter tolerances can increase cost.
• Confirm datum scheme, material condition modifiers and inspection access with the design/quality team.

## Slide 27
MODULE 07
Manufacturing-aware design
Use CAD to help prevent production problems before parts are made.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
27

## Slide 28
7.1 Design for manufacturing (DFM)
Model the part that can be made, inspected and assembled
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
28
• Machining: check tool access, internal corners, hole depth, setups and clamping.
• Sheet metal: check bend relief, minimum flange length, bend radius and flat pattern.
• Welding: consider weld access, joint preparation, distortion and inspection.
• Moulded parts: consider draft, wall thickness, ribs, bosses, gates and ejection.
• Assembly: provide locating features, fastening access, poka-yoke and service clearance.
• Use material, process and finish requirements that match the intended supplier and specification.

## Slide 29
7.2 Simulation and validation
Simulation is a decision-support tool — validate assumptions and results
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
29
• Define the question first: stress, displacement, thermal behavior, motion or flow.
• Assign realistic materials, contacts, fixtures and loads.
• Use a suitable mesh; refine where gradients or stress concentrations are important.
• Check units, boundary conditions, reaction forces and whether results make physical sense.
• Run mesh/convergence checks for important studies and document assumptions.
• Confirm critical designs with appropriate engineering review and physical testing.

## Slide 30
MODULE 08
Productivity and professional workflow
Use repeatable habits to make your models faster to edit and easier to release.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
30

## Slide 31
8.1 Professional workflow checklist
Before sending a CAD package to another person or supplier
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
31
Sketches and feature tree are understandable
All features rebuild without errors or warnings
Units, materials and custom properties are correct
Part/assembly references are not missing
Interferences and clearances are reviewed
Drawing views, dimensions and tolerances are complete
Revision, title block and filenames are correct
Neutral export (STEP/PDF/DXF as required) is checked after export

## Slide 32
8.2 Keyboard and modeling habits
Shortcuts vary by setup; customize them to match your daily work
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
32
• Use S for the shortcut bar in many SOLIDWORKS setups; customize it for your workflow.
• Use Ctrl+8 for Normal To; use standard view controls to orient sketches and models.
• Use the mouse wheel to zoom; middle mouse button to rotate in common default settings.
• Use rollback and suppress carefully when diagnosing a feature-tree problem.
• Create templates for units, drafting standards, title blocks and material properties.
• Learn search and command discovery so you can find unfamiliar tools quickly.

## Slide 33
MODULE 09
Capstone project
Apply the complete workflow by designing a simple machine fixture or mounting assembly.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
33

## Slide 34
Capstone: design a small fixture
Example scope — adapt dimensions to your own safe training brief
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
34
Part files
Base plate, support blocks, locating pins, clamps and fasteners.
Assembly
Mate parts, check movement, access and interference.
Drawing pack
Part drawings, assembly drawing, BOM and exploded view.
• Deliverable 1: organized feature tree and editable part files.
• Deliverable 2: assembly with sensible mates and no unintended interference.
• Deliverable 3: manufacturing drawings with dimensions and tolerances.
• Deliverable 4: neutral export and a short design review explaining key decisions.

## Slide 35
10-week practice plan
Consistency beats watching tutorials without building models
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
35
Week | Focus | Practice output
1 | Interface, navigation, units, sketch relations | 5 simple sketches
2 | Dimensions, fully defined sketches, constraints | Plate with holes
3 | Extrude, cut, revolve, fillet, chamfer | Mounting block
4 | Patterns, mirrors, Hole Wizard, design intent | Flanged bracket
5 | Assembly basics and mates | Pin-and-bracket assembly
6 | Drawings, sections, dimensions, BOM | Drawing pack
7 | Sheet metal and flat patterns | L-bracket
8 | Weldments, configurations, equations | Frame or size variants
9 | Advanced part tools, surfaces, validation basics | Selected advanced model
10 | Capstone, review, portfolio and exports | Complete design package
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
35

## Slide 36
Practice challenges
Try these without copying a video step-by-step
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
36
Beginner
Create a 100 × 60 × 10 mm plate with four mounting holes. Fully define the sketch.
Intermediate
Build a shaft support with a revolved profile, mounting holes and a drawing.
Advanced
Create a small adjustable fixture assembly with mates, configurations and BOM.
For every challenge: save the native files, capture a clean isometric view, create a drawing and explain why you chose each feature.
Self-check: Can you change a key dimension without breaking the model?

## Slide 37
Official learning resources
Use this deck with the official tutorials and help documentation
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
37
SOLIDWORKS Tutorials channel
Step-by-step videos for beginner through advanced workflows.
youtube.com/@solidworkstutorials_official
In-software Tutorials
Open Help → SOLIDWORKS Tutorials (menu wording varies by version).
help.solidworks.com
Official training courses
Design essentials, drawings, assemblies, advanced parts, sheet metal and more.
solidworks.com/support/training/classroom-training-courses
Beginner's guide
Start with sketches, parts, holes, assemblies and revisions.
blogs.solidworks.com/products/solidworks/beginners-guide-to-solidworks/
Official resources may describe features that depend on your SOLIDWORKS version or license.
SOLIDWORKS LEARNING PATH • BEGINNER → ADVANCED
37

## Slide 38
YOUR NEXT STEP
Open SOLIDWORKS. Build one part today.
Start with a fully dimensioned sketch, create a simple feature, save the file, and repeat until the workflow feels natural.
Learn the tool • understand the engineering • practice the workflow
38